## Slide 1: Sockets over RDMA
Arkady Kanevsky
Network Appliance

## Slide 2: Three legged stool
Protocol
APIs
Interoperability/Backward compatibility

## Slide 3: Protocol License issues
MSFT SDP patents
  http://www.microsoft.com/about/legal/intellectualproperty/standards/default.mspx
    SDP over IB
    each company signs 1-on-1 source code license agreement with MSFT for development of SDP.
      SDP source code must include MSFT “license” statement
      No license for 3rd party or distributors
  kernel.org will not accept SDP code under these conditions.

## Slide 4: API
MSFT Windows Socket Direct was extended to exposed memory registration
OpenGroup ICSC Extended Socket API
Need for common simple Socket over RDMA API
  proper semantic mapping of socket semantic to RDMA
  user API with kernel bypass
  kernel API

## Slide 5: SDP Protocol Technical
SOCK_STREAM in SDP (RC-based)
SOCK_DGRAM not is SDP
SDP 4 data transfer methods
  combined into modes: buffered, pipelined, combined
SDP CM manager is not based on IBTA RDMA IP CM Service Annex (post IBTA 1.2)
  assigned SID
  Single QP
Flow control
No true zero-copy in OFA SDP implementation

## Slide 6: Michael Tsirkin’s Protocol comments
Hard to fix issues that seem to be fundamental in SDP mode of operation.
No support for SRQ - forces pre-posting of large number of buffers per-socket.
Low connection rate - a single connection can't be reused for multiple sockets
SW-based credits don't utilize hardware flow control, and break polling-based operation
No support for high availability: failover only with APM
No support for multicast and/or UDP (discard packets on RQ overrun).
Issues that might be addressable with extensions to the SDP protocol.
SDP Zcopy mode not a good fit for synchronous operations (Zcopy read needs slow 3 way handshake, zcopy write can not pipeline many writes into a single
advertisement)
mode-based operation - can't mix RDMA (for large buffers) and bcopy (for small buffers)
OOB not supported in zcopy mode
SDP connection setup it too different from TCP socket setup, so SDP termination/routing across a TCP socket quite non trivial.
“Lost RTU" problem - analog of SYN flood (seen when remote is unstable/crashing).

## Slide 7: Interoperability
What about interoperability with SDP?

## Slide 8: New Protocol needed or not?
What are the requirements?
Let the discussion start…