## Slide 1: OFA-IWG Interop Event April 2007
Rupert Dance
Lamprey Networks
Sonoma Workshop Presentation

## Slide 2: Agenda
Event Overview
Program Details
Vendor Participation
Device Categories
Devices Tested
Test Environment
Mandatory versus Beta testing
Cluster Topology
Problems Noted
Summary

## Slide 3: Event Overview
IBTA IL Compliance Testing 4/11/07 4/13/07
  8 vendors, 13 devices and 35 cables tested
  This was the 11th IBTA Plugfest
OFA IWG Interop Event 4/16/07  4/20/07
  6 vendors, 22 devices and 31 nodes tested
  This is the second official OFA-IWG Interop event
Hosted by University of NH Interoperability Lab (UNH-IOL)
Overall results very successful
Next event scheduled for October 2007

## Slide 4: Program Details
IBTA integrators List
  This list includes all products that have successfully completed the rigorous testing procedures at IBTA sponsored Plugfests.
  Current List of devices is available at http://www.infinibandta.org/itinfo/IL
  Updated list will be available in May 2007
OFA-UNH-IOL Logo Program
  Enable vendors to claim and market interoperability by using the Logo on their products or in their product marketing collateral.
  Details available at http://www.iol.unh.edu/services/testing/ofa/logo.pdf
  List of Logo Grants will be available in May 2007

## Slide 5: Vendor Participation
InfiniBand
  Cisco, Data Direct, Flextronics, Mellanox, QLogic, Voltaire
iWARP
  Chelsio and NetEffect
Test Equipment Vendors
  Anne, Finisar and Tektronix

## Slide 6: Device Types and Categories
InfiniBand
  9 HCAs running OFED 1.2 RC1
  8 IB Switches
  1 iSER Target
  1 SRP Target
  5 SMs
    Host Based SMs: OpenSM, Voltaire
    Switch Based SMs: Cisco, QLogic, Voltaire
iWARP
  Two R-NICs

## Slide 7: InfiniBand Devices Tested
Cisco
  SFS 7000D - 24-port DDR Switch
  SFS 7008 - 96-port SDR Switch
Data Direct
  S2A 9550 - IB SRP connected storage system
Flextronics
  F-X430066 - 8-Port SDR 4-X InfiniBand switch
  F-X430044 - 24 Modular DDR 4-X InfiniBand switch
  F-X430081 - 144 Modular DDR 4-X InfiniBand switch
Mellanox
  MHEA28-1TC - Dual-port, 10Gb/s w/ media adapter support, PCIe x8, 128MB memory
  MHEA28-XT - Dual-port, 10Gb/s w/ media adapter support, PCIe x8, mem-free
  MHGA28-1TC - Dual-port, 20Gb/s w/ media adapter support, PCIe x8, 128MB memory
  MHGA28-XTC - Dual-port, 20Gb/s w/ media adapter support, PCIe x8, mem-free
  MHES14-XT - Single-port, 10Gb/s w/ media adapter support, PCIe x4, mem-free
  MHES18-XTC - Single-port, 10Gb/s w/ media adapter support, PCIe x8, mem-free
  MHGS18-XTC - Single-port, 20Gb/s w/ media adapter support, PCIe x8, mem-free
QLogic
  QHT-7140 - InfiniPath QHT 7000 Series
  QLE-7140 - InfiniPath QLE 7000 Series
  9024-CU24-ST2-DDR - SilverStorm 24 port 1U DDR 4x Switch\
Voltaire
  ISR 2012 - 288 ports infiniband Grid Director
  ISR9024D-M - 24 ports infiniband Grid Swith
  SMHost-3.4.8-110 - SMHost (GVFM) - 4.4.8-110
  IPStor - iSER target (IPStor) - 5187
  GridStack 4.1 - GridStack-4.1.5_6
  GridStack Window - Windows GridStack - 2.5.615.741

## Slide 8: iWARP Devices Tested
Chelsio
  S310 - 10 Gig Unified Wire Ethernet NIC (NIC, TOE, iSCSI, iWARP)
NetEffect
  NE020 - NES Dual-port 10GE RNIC

## Slide 9: Test Environment
RHEL 5 and SLES 10 SP1
OFED 1.2 RC1
13 Intel provided severs
Cables provided by the following vendors
  Amphenol
  Fujikura
  W.L. Gore
  Zarlink
Test equipment providers
  Anue Systems - http://www.anuesystems.com/
  Finisar - http://www.finisar.com/home.php
  Tektronix - http://www.tek.com/

## Slide 10: Mandatory versus Beta Testing
Test Status for April 2007 Interop Event |  |  | 
Test Procedure | InfiniBand Devices | iWARP Devices | Transport Independent
IB Link Initialize | Mandatory | Not Applicable | 
IB Fabric Initialization | Mandatory | Not Applicable | 
IB IPoIB | Mandatory | Not Applicable | 
TI iSER |  |  | Beta
IB SRP | Mandatory | Not Applicable | 
TI SDP | Mandatory | Beta | 
IB SM Failover/Handover | Beta | Not Applicable | 
TI MPI - OSU |  |  | Beta
TI MPI Intel |  |  | Beta
TI uDAPL |  |  | Beta
IWARP Connectivity | Not Applicable | Mandatory | 
Fibre Channel Gateway (IB) | Beta | Not Applicable | 
Ethernet Gateway (IB) | Beta | Not Applicable | 

## Slide 11: Recommended Test Status for October 2007 Interop Event
Test Procedure | Review status | Recommended Status
IB Link Initialize | Well tested | Mandatory
IB Fabric Initialization | Well tested | Mandatory
IB IPoIB | Well tested | Mandatory
TI iSER | Some issues to be resolved | Beta
IB SRP | Well tested | Mandatory
TI SDP | Well tested | Mandatory
IB SM Failover/Handover | Some issues to be resolved | Beta
TI MPI - OSU | Needs more testing | Beta
TI MPI Intel | Needs more testing | Beta
TI uDAPL | Some issues to be resolved | Beta
IWARP Connectivity | Well tested | Mandatory
Fibre Channel Gateway (IB) | Needs devices to run tests | Beta
Ethernet Gateway (IB) | Needs devices to run tests | Beta

## Slide 12: Cluster Topology

## Slide 13: Problems Noted
Needed more time for Compliance and Interop testing. Suggested format
  Week one
    Monday through Wednesday
      IBTA and iWARP compliance testing
    Thurs-Fri
      Interop cluster setup
      InfiniBand Link and Fabric Init
  Week two
    iWARP Connectivity, IPoIB, SDP, SRP, iSER, SM Failover, Gateway Tests, DAPL and MPI
Vendor review and input on the Test Plan is needed because it may affect their Logo Grant.

## Slide 14: Problems Noted - Continued
A link problem was discovered during the Link Init Test
Tests requiring one to many testing are very time consuming. Need automated scripts
  IPoIB
  SRP
  SDP
  iSER
iSER – possible issues with the OFED Stack code
uDAPL
  Single switch testing ran reasonably well but there were some unpredictable failures.
  Multiple switch tests experienced some problems
We need 30-50 DDR cables dedicated to the cluster
We need to coordinate the Interop Event with the OFED Releases

## Slide 15: Summary
Best Interop Event to date
  Considerable progress made on the Interop Plan
  Test Scripts much improved
  Test execution went smoothly
  UNH-IOL staff performed very well
Mandatory testing was very successful
Beta testing
  Need device participation in some categories such as FC and Ethernet Gateway devices
  Need more SRP targets
Need more time to complete all of the testing