## Slide 1: iWARP in OFED 1.2 Asgeir Eiriksson Chelsio Communications Inc. April 30, 2007 OFA Workshop, Sonoma
Notes: <number>
3rd OFA Workshop April 30, 2007, Sonoma

## Slide 2: Introduction
Chelsio’s T3 Unified Wire Ethernet engine
OFED 1.2 stack and iWARP
  Part of upstream kernel 2.6.21
  Beta release imminent
Testing & performance results
Conclusions & what’s next
Notes: 3rd OFA Workshop April 30, 2007, Sonoma
<number>

## Slide 3: Chelsio T3 Unified Wire Engine
Native PCIe x8 and PCI-X 2.0 interfaces
2 x 10Gbps Ethernet ports
Simultaneously, one adapter operates as:
  NIC
    Plugs into the TCP/IP network stack as a high performance NIC
  iSCSI
    Plugs into the storage stack as a 10Gbps iSCSI device
  iWarp
    Plugs into OFA as a high performance iWARP RDMA RNIC
  TOE
    Accelerates TCP/IP applications with full TCP/IP offload
3rd generation offload engine
Integrated traffic manager
Notes: 3rd OFA Workshop April 30, 2007, Sonoma
<number>

## Slide 4: Chelsio Unified Wire: PCI Bus
<number>
S320e-XFP
S320e-CX
S310e-CX
S302e
S302x
S321e-CX
S320x-XFP
Notes: <number>

## Slide 5: Chelsio Unified Wire: Offload NIC
Features
  Checksum offload
  TSL/LSO (Send Large Segment Offload)
  LRO (Receive Large Segment Offload)
  RSS (Receive Side traffic Steering)
  SSS (Send Side Scaling)
Performance
  10Gbps line rate TX
    1500B frames, or 9KB jumbo frames
  10Gbps line rate RX
    1500B frames, or 9KB jumbo frames
  Zero copy for TX possible
  Zero copy for RX NOT possible
Notes: 3rd OFA Workshop April 30, 2007, Sonoma
<number>

## Slide 6: Chelsio Unified Wire: iSCSI
Features
  iSCSI on top of TCP/IP
  iSCSI header and data digest (CRC) offload
  TX DDP
    Zero copy send and iSCSI encapsulation
  RX DDP
    Zero copy receive of iSCSI payload
  Boards support 32K connections (chip up to 1M)
Measured Performance
  BW 10Gbps bidirectional
  900+K IOPS rate (512B transfers)
Notes: 3rd OFA Workshop April 30, 2007, Sonoma
<number>

## Slide 7: Chelsio Unified Wire: TOE
Features
  Accelerates classical sockets API
  TX DDP
    Zero copy send
  RX DDP
    Zero copy receive
  Boards support 32K connections (chip up to 1M)
Performance
  Line rate 10Gbps bidirectional
  ~7us end-to-end application-to-application latency
    Interrupt driven receive, less for polling receive
  < 5% CPU for transmit
  < 5% CPU for receive
Notes: 3rd OFA Workshop April 30, 2007, Sonoma
<number>

## Slide 8: Chelsio Unified Wire: TOE
<number>
High-performance architecture
  10Gbps wire rate from 1 up to 10s of thousands of connections
  Low latency cut-through processing for transmit and receive
  10Gbps wire rate filtering and virtualization
Full TCP Offload Engine
  Connection setup/teardown
  Fast retransmit, timeout retransmission, congestion control
  Out-of-order packet handling and exception handling
  All TCP timers and probes
  Listening server offload (full bit-wise wildcards)
  Extensive RFC compliance
  Internet attack protection
Notes: <number>

## Slide 9: Chelsio Unified Wire: iWARP RDMA
<number>
Standards-compliant RDMA
  IETF RDDP
  RDMAC iWARP 1.0
  Strict/permissive interoperability of IETF RDDP & RDMAC standards
Software interfaces
  OFA
  Supports OS-bypass and optional polling receiver
Embedded microprocessor
  Work request & error management
Features
  64K queue pairs
  64K doorbells
  64K completion queues
  64K protection domains
  Hardware-based STAG management
  Fully cache coherent polling receiver
Notes: <number>

## Slide 10: What’s in the Box
<number>
Notes: <number>

## Slide 11: Unified Wire: Traffic Manager
<number>
Multiple transmit and receive queues with 8 QoS classes
  8 transmit queue sets with configurable service rates
  8 receive queue sets with configurable steering of receive traffic
  Each class can have any number of connections
Two priority channels through chip for simultaneous low latency and high bandwidth
Advanced traffic shaping and pacing
  Eliminates TCP burstiness issues
  Fine grained per-connection transmit rate shaping
  Fine grained per-class transmit rate shaping
Highly flexible and configurable
  Fixed per-connection or per-class bandwidth – possible to mix both
    For example: one corresponding to 5.5Mbs MPEG, another to teleconferencing, etc.
  Traffic Type, TOS and DSCP mapping
  Configurable weighted-round-robin scheduler to enforce SLAs
Notes: <number>

## Slide 12: Chelsio OFED 1.2 Support
Available at kernel.org
  in 2.6.21 today
  drivers/net/cxgb3 – Ethernet Driver
  driver/infiniband/hw/cxgb3 – RDMA Driver
Open Fabrics Enterprise Distribution (OFED)
  Version 1.2
  Beta Released 4/2007
Dual BSD/GPL License
Stable
  In performance QA now
  Looking at performance corners
Notes: <number>

## Slide 13: Chelsio OFED 1.2 Modules
cxgb3
  Ethernet NIC
  TCP Offload NIC
iw_cxgb3
  RDMA Provider
  Depends on cxgb3
Full offload TCP/IP
  Connection setup in hardware
HW Services
Notes: <number>

## Slide 14: OFED 1.2
Based on 2.6.20 RDMA code + fixes
Platforms: X86_32, X86_64, IA64, PPC64
kernel.org 2.6.21 Support
Distros Support:
  RHEL4 U4/5, RHEL5, SLES9SP3, SLES10 SP0/1
  To be released with SLES 10SP1 and RHEL5
SRPM, RPM Packaging
Notes: <number>

## Slide 15: OFED 1.2 Kernel Modules
Infiniband (IB)
  Mellanox, IBM, QLogic HCAs
  IP over IB (IPoIB)
  Sockets Direct Protocol (SDP)
  SCSI RDMA Protocol (SRP), iSCSI RDMA (iSER)
  Reliable Datagram Service (RDS)
  Virtual NIC (VNIC)
  Connection Manager (IBCM)
  Multicast
Notes: <number>

## Slide 16: OFED 1.2 Kernel Modules
iWARP
  Chelsio RNIC
  iWARP Connection Manager
RDMA-CM
Notes: <number>

## Slide 17: OFED 1.2 User Components
Direct Access Provider Library (uDAPL)
Message Passing Interface (MPI) Support
  MVAPICH, MVAPICH2 (in QA)
  OpenMPI (panned)
IB Subnet Management via OpenSM
Connection Management
  RDMA-CM
  IB-CM
Notes: <number>

## Slide 18: OpenFabrics Software Stack
RDMA NIC
R-NIC
Host Channel Adapter
HCA
User Direct Access Programming Lib
UDAPL
Reliable Datagram Service
RDS
iSCSI RDMA Protocol (Initiator)
iSER
SCSI RDMA Protocol (Initiator)
SRP
Sockets Direct Protocol
SDP
IP over InfiniBand
IPoIB
Performance Manager Agent
PMA
Subnet Manager Agent
SMA
Management Datagram
MAD
Subnet Administrator
SA
Common
InfiniBand
iWARP
Key
InfiniBand HCA
iWARP R-NIC
Hardware
Specific Driver
Hardware Specific
Driver
Connection Manager
MAD
InfiniBand OpenFabrics Kernel Level Verbs / API iWARP R-NIC
SA Client
Connection
Manager
Connection Manager
Abstraction (CMA)
InfiniBand OpenFabrics User Level Verbs / API iWARP R-NIC
SDP
IPoIB
SRP
iSER
RDS
SDP Lib
User Level MAD API
Open SM
Diag
Tools
Hardware
Provider
Mid-Layer
Upper Layer Protocol
User APIs
Kernel Space
User Space
NFS-RDMA
RPC
Cluster
File Sys
Application Level
SMA
Clustered
DB Access
Sockets
Based Access
Various
MPIs
Access to
File
Systems
Block
Storage
Access
IP Based
App
Access
Apps & Access Methods for using OF Stack
UDAPL
Kernel bypass
Kernel bypass
Notes: <number>

## Slide 19: OFA/OFED APIs
Open Fabrics Verbs
  Minimal changes from IB API to support iWARP
  Needs iWARP-specific verb support
Open Fabrics RDMA-CM
  Transport neutral connection setup
  IP address / port based
Kernel and User Interfaces
  User interface supports kernel-bypass
Notes: <number>

## Slide 20: IB vs. Chelsio Ethernet iWARP
<number>
Chelsio T3 RNIC
  Simultaneous OFED 1.2, iSCSI over TCP/IP, TOE, NIC
IPoIB
  T3 all in one NIC, iSCSI HBA, and iWARP RDMA
  IPoIB handled with NIC and TOE on Ethernet side
SDP
  IB implementation of classical socket API
  T3 also has this functionality via DDP TOE
  DDP TOE is API compatible with classical sockets API
SRP
  T3 also supports iSCSI over TCP/IP which has its own built-in DDP mechanism
Notes: <number>
3rd OFA Workshop April 30, 2007, Sonoma

## Slide 21: iWARP OFED 1.2: Testing
Third generation TCP offload
  Extensively tested
iWARP testing completed
  Internal Test Bed
    Long running stress tests
  uDAPL test suite
    Passing
  NFS over RDMA
    Passing
  MPI
    No correctness issues
    Performance testing ongoing
  UNH conformance testing
    Completed
Notes: 3rd OFA Workshop April 30, 2007, Sonoma
<number>

## Slide 22: OFA/OFED 1.2 : Performance
Internal Measurements
  Throughput
    Consistently hits full line rate 10Gbps bidirectional
  Latency
    RDMA READ latency in the 4-6usec range (depending on the platform)
    RDMA WRITE latency in the 6-7usec range (depending on the platform)
  Low CPU utilization
MVPICH MPI
  DK Panda et al. at OSU will be presenting performance results with Chelsio today.
NFS over RDMA
  Helen Chen et al. at Sandia will be presenting performance results with Chelsio tomorrow.
Notes: 3rd OFA Workshop April 30, 2007, Sonoma
<number>

## Slide 23: Chelsio T3 iWarp Latency

## Slide 24: Chelsio T3 iWarp Throughput

## Slide 25: Conclusions
<number>
Chelsio has stable OFED 1.2 iWARP RNICs available and shipping today
  Line rate 10Gbps bidirectional
  End-to-end latency in 4-7us range depending on platform
    Cut-through processing key to these latency numbers
  Low CPU utilization
  Extensive QA testing done, and performance QA is on-going
Unified Wire Engine
  Builds on 3rd generation protocol offload
Integrated Traffic Manager
Notes: <number>
3rd OFA Workshop April 30, 2007, Sonoma

## Slide 26: Next
The 10G Ethernet TCP testing has been limited to small clusters up to this point 4-12 nodes
  TCP congestion control scales in robust fashion
    Full line rate is maintained
    Over-subscribed receivers are not an issue
  Burstiness and lack of Traffic Management was an issue
    e.g. 10Gbps sender can overwhelm a slower receiver such as a block or file storage system
People are starting to assemble RNIC clusters consisting of 100s of nodes
  We expect Traffic Management and Traffic Engineering to play a significant role in large RNIC clusters
  With the help of Traffic Management and Engineering, we expect TCP congestion control to scale in robust fashion in large clusters
Notes: 3rd OFA Workshop April 30, 2007, Sonoma
<number>

## Slide 27: Thank You
<number>
Notes: <number>
3rd OFA Workshop April 30, 2007, Sonoma