## Slide 1: Operational and Application Experiences with the Infiniband Environment
Sharon Brunett
Caltech
May 1, 2007

## Slide 2: Outline
Production Environment using Infiniband
  Hardware configuration
  Software stack
  Usage model
Infiniband particulars
  Sample application
  Benchmarks
  Issues
A less challenging future
  A collection of hoped for improvements

## Slide 3: Opteron/Infiniband Cluster Configuration
Extreme Networks
Black Diamond 8810
Copper GigE
8 GB memory
2.2 GHz
256 GB scratch
86 dual CPU, dual core
AMD Opteron nodes
Voltaire Infininband
Switch
16 GB memory
2.2 GHz
quad CPU, dual core
AMD Opteron head/login node
(shc.cacr.caltech.edu)
8
~ 25 TB
/pvfs/data-store02
~ 25 TB
/pvfs/data-store03
8 GB memory
2.4 GHz
256 GB scratch
38 dual CPU, dual core
AMD Opteron nodes
8
…124…
:
124
:
~ 24 TB (RAID6)
/nfs/data-store01
Opteron dual CPU
dual core, 16 GB
NFS server

## Slide 4: Compute Resource Utilization Summary
Even balance between active projects
76% utilization for 2007
  up from 64.9% in 2006
Mix of development and production jobs
  Typically ranging in size from 4 to 32 nodes, 2 to 24 hours
Approx 100 user accounts, 5 partner projects

## Slide 5: Production Environment
Software stack impacting Golden Image
  SLES9 (security patched) kernel version 2.6.15.9
  Mellanox Infiniband drivers v3.5.5
    No sources available to us
  Parallel Virtual File System (pvfs) v2
  OpenMPI (2.1.X)
  Torque
  Maui
Software stack - user tools
  Plotting and Data Visualization Tool - Tecplot
  Debugger - Totalview
  Numerical Computing Environment/language - Matlab
  Portable Extensible Toolkit for Scientific Computation - PETSc
  Hierarchial Data Format (HDF) v4,5

## Slide 6: SCS Grains Simulation
Highly resolved simulations of shear compression polycrystal specimen tests
Production run stats
  LLNL’s alc, 12 hours 118 CPUs, 900K steps, 4.4 GB of dumps

## Slide 7: Sample Application MPI profile
As problem size grows, MPI impact less due to better load balancing
  MPI_Waitall and AllReduce are major time consumers
  Run smaller benchmarks for tuning suggestions

## Slide 8: PMB PingPong
Notes: Classic pattern used for measuring startup (latency) and throughput (bandwidth) of a single message sent between two processes

## Slide 9: PMB PingPong

## Slide 10: PMB MPI_AllReduce

## Slide 11: Tuning Tests Revealed Infiniband Issues
The Port Management (PM) facility gives sysadmin/user ability to analyze and maintain the Infiniband environment
  Particular ports had high PortRcvErrors, indicative of a bad link
    Moving cables and swapping in a new IB blade isolated the problem further
  Congestion reduced by configurable threshold limit (HOQlife)

## Slide 12: Problem IB Blade Identified New Challenges Arise
Servicing the Infiniband switch, as currently installed, is no picnic
  Note how working parts need to be dismantled to access parts needing service
    Cable tracing and stress needs attention
  Line boards can take multiple re-seatings before they’re “snug”
As Mark says…hardware should be treated like a delicate flower

## Slide 13: Lessons Learned
Sections of the code with MPI collective calls sensitive to msg lengths and process counts
  Run indicative benchmarks as part of production run set up process
Use Voltaire’s PM utility to routinely monitor the fabric for problems
  Functionality and performance
Buy dinner for Trent and Ira
  test out linkcheck and ibcheckfabric on our little cluster

## Slide 14: Making our Lives Easier
Mellanox drivers -> OpenIB ?
  Locally built golden image gives flexibility but has drawbacks
Automatic probing of PM counter report files to compare against “known good” states
  Report suspect components
Use standard/factory benchmarks to verify Infiniband cluster is working at customer site as well as when the integrated system shipped!
  Increasingly important as cluster expands
  Incorportate low level PM facilities into support level tools for better integrated monitoring