## Slide 1: High Availability through the Linux bonding driver
Or Gerlitz
Voltaire
ogerlitz@voltaire.com

## Slide 2: agenda
bonding driver background / concepts
bonding driver high availability mode
bonding IPoIB devices – status
slaves requirements for a bond
enabling High-Availability for native IB ULPs
bonding IPoIB devices – code changes
  ipoib HW address
  bonding driver changes
  ipoib HW address - revisited
  ipoib driver changes

## Slide 3: bonding driver background
bonding (master) device that enslaves other devices
the local system/stack (addressing, routing, multicast) interact only with the bond device
bonding supports both HA and LB, we focus on HA
code path: drivers/net/bonding
doc path: Documentation/networking/bonding.txt

## Slide 4: bonding driver HA mode
called Active-Backup
bonding has one active slave, applies link detection mechanisms to trigger fail-over
one HW (L2) address is used for the bond
typically the one of the first slave, which is then assigned to the other slaves as well

## Slide 5: bonding HA mode – cont’
link detection mechanisms
  local: uses the carrier bit of the slaves
  path validation: implemented through an ARP target to which probes are sent
fail-over
  bonding sends a Broadcast Gratuitous ARP (originally to update the Ethernet switches tables)
  bonding does a “replay” of multicast join

## Slide 6: bonding of IPoIB devices - status
some changes were required in the bonding driver and some in the ipoib driver
bonding changes – patch set passed two review cycles at netdev
ipoib changes – patch accepted to OFED 1.2 –some issues pending for upstream push
configuration issues still persist
the solution is integrated into OFED 1.2

## Slide 7: slaves requirements for a bond
slaves must be of the same ether type
  you can’t bond ipoib and non-ipoib interfaces
slaves must use the same partition (VLAN)
  you can’t bond ib0.8003 with ib1.8004
slaves can be of different mode (UD vs CM)
  however, slaves MTU must be normalized

## Slide 8: high-availability for native IB ULPs
bonding provides HA at the Link (L2) level
basically, layer separation means that TCP sessions should not break, but they can
HW failure would cause the IB RC session of a native IB ULPs (SDP, RDS, iSER, Lustre, rNFS) to break
  bonding allows for a new session to be established immediately (as ipoib is the IB stack [rdma_cm] ARP provider)
  depending on the ULP, this session breakage may not be even seen by the user!

## Slide 9: bonding/IPoIB code changes
details follow

## Slide 10: IPoIB HW address
20 bytes
  1 byte - supported IB transports (bitmap)
  3 bytes – the UD QP number
  16 bytes – the IB port GID (made of an eight bytes subnet prefix & eight bytes port GUID)
the GUID is unique and has to be distinct from the view point of the SM
the QP is a resource allocated by the HCA and is always distinct

## Slide 11: bonding driver changes
problem: enslave devices whose HW address can’t be assigned from the outside
  solution: the bond HW address is the one of the active slave
problem: enslave devices whose ether type is not ARPHRD_ETHER
  solution: override some of ether_setup settings with the slave ones (ether type, broadcast addr, HW addr len, HW header len, neighbour setup function etc)

## Slide 12: IPoIB HW address - revisited
IB UD L2 address is made of AH & QPN
  hence the 20 bytes HW neighbour address exposed by ipoib to the stack is not what the driver really uses
ipoib uses a two layer neighboring scheme, such that for each struct neighbour there is a struct ipoib_neigh buddy
  ipoib installs a neighbour cleanup callback used to free the ipoib_neigh buddy resources

## Slide 13: IPoIB driver changes
under bonding neighbours are created on behalf of the bond device, hence -
problem: under bonding the ipoib neighbour destructor can’t assume that n->dev is an ipoib device
  solution: add pointer to the device in struct ipoib_neigh and use this pointer in the cleanup func

## Slide 14: bonding/IPoIB changes - summary
bonding: the bond HW address is the one of the active slave (if the slave doesn’t support assignment)
bonding: override some of ether_setup settings with the slave ones (if the slave is not of ARPHRD_ETHER type)
ipoib: add pointer to the device in struct ipoib_neigh and use this pointer in the cleanup func

## Slide 15: open issues
upstream push
  neighbour cleanup after slave module unload
  following a bonding fail over packet xmit over the new active slave, which happens before the old slave flushed the ipoib neighbours
configuration tools
  an old and deprecated user tool named ifenslave is used, which can be now replaced by a script using the bonding sysfs entries