## Slide 1
Adventures Installing Infiniband Storage
Randy Kreiser Chief Architect
Sonoma OpenFabrics Workshop 1 May 2007
Notes: <number>

## Slide 2: Meet the Players (Hardware)
Host Channel Adapters & Switches
  Mellanox
  Qlogic
  Voltaire
  Cisco
Storage
  Data Direct Networks
  Engenio
  Texas Memory (SSD)
  Others?

## Slide 3: Meet the Players (Software)
Infiniband Drivers
  OFED
  Mellanox IBGLD
  Qlogic
  Voltaire
  Cisco
Subnet Manager
  OpenSM
  Qlogic
  Voltaire
  Cisco

## Slide 4: Decisions, Decisions, Decisions
What operating system am I using
  SuSe
  RedHat
  Other?
What HCA should I use?
  PCI-x
  PCI-e
What switch should I use?
  Port count?
What initiator driver should I use?
  Performance ???
  Compatibility
  Failover
What storage should I use?
  Performance ???
    IOPS
    Bandwidth

## Slide 5: Decisions, Decisions, Decisions
SRP or iSER drivers
Which subnet manager should I use?
Where should the subnet manager run?
  Switch
  Host
Troubleshooting
  I can’t see any luns
Benchmarking
  600MBS
  800MBS
  1000MBS
  2000MBS

## Slide 6: Direct Connect
1
2
3
4
5
6
7
0
P1
P2
Tier
1
Tier
2
Tier
3
Tier
4
Tier
5
Tier
6
Tier
7
Tier
8
HCA
DCE
HCA
HCA
HCA
HCA
HCA
Test Host
IB
4
X
FCAL
S2A Controller 1
S2A Controller 2

## Slide 7: Benchmarking
O_Direct I/O vs non O_Direct I/O
  Large Sequential I/O
  Small Random I/O
Software Striping
  Chunk Size
Block device max sectors
  MAX SECT
  SG_TABLE_SIZE
Block device read ahead
  hdparm
  blockdev
Queue Depth
  Setting
RAID Controller Settings
  Cache Size

## Slide 8: Benchmarking
Write performance
blk size | /dev/sdc | c+d+e+f
256MB | 686.56 | 2527.49
128MB | 684.54 | 2473.39
64MB | 677.64 | 2375.96
32MB | 673.22 | 2223.60
16MB | 660.31 | 1967.58
8MB | 638.19 | 1614.75
4MB | 587.30 | 1336.12
2MB | 523.75 | 792.44
1MB | 419.26 | 420.73
512KB | 314.54 | 317.76
256KB | 217.89 | 221.72
128KB | 151.55 | 154.67
Read performance
blk size | /dev/sdc | c+d+e+f
256MB | 616.66 | 1793.89
128MB | 603.98 | 1677.27
64MB | 596.96 | 1573.50
32MB | 583.34 | 1461.18
16MB | 594.86 | 1414.46
8MB | 575.79 | 1298.77
4MB | 535.69 | 1112.40
2MB | 476.80 | 672.72
1MB | 386.84 | 366.45
512KB | 295.09 | 288.99
256KB | 213.43 | 208.64
128KB | 158.39 | 158.00

## Slide 9
Supported Disk Technology | SAS & SATA | FibreChannel & SATA
RAID Parity Protection | RAID6 8+2 Only | RAID3 (8+1+1), RAID6 8+2
Sustained Throughput | 5.6GB/s – 6.0GB/s | 2.4 GB/s – 2.8GB/s
Maximum Cache | 5.0 GB ECC Protected | 2.5GB RAID Protected
Minimum Cache | 2.5 GB ECC Protected | 2.5GB RAID Protected
Disk Side Ports | 20 x SAS 4 Lane | 20 x FC-2
Host Side FC Ports | 8 x IB 4x DDR or 8 x FC-8 | 8 x FC-4 or 8 x IB 4x
Dimensions | 7 x 19 x 28 in. (4U) | 7 x 19 x 25 in. (4U)
Certifications | UL,CE,CUL,C-Tick,FCC | UL,CE,CUL,C-Tick,FCC
Release Date | 1Q/2008 | September 2005
Specification S2A9900 Couplet S2A9550 Couplet
S2A 9900 Hardware Specifications (What’s Next)

## Slide 10: SRP
SRP

## Slide 11: SRP (SCSI RDMA Protocol)
Advantages
  Inifiniband native protocol
  No new hardware required
  Requests carry buffer information
  All data transfer through Infiniband RDMA
  No Need for Multiple Packets
  No flow control for data packets necessary

## Slide 12: Direct Connect Example
IB ports with direct connections
Data distribution through servers
Asymmetrical file systems (Lustre, etc.)

## Slide 13: SRP General
SCSI RDMA Protocol
  SCSI over IB
  Similar to FCP (SCSI over Fibre Channel) except that CMD Information Unit includes addresses to get/place data.
  Initiator drivers available with IB Software Vendors and OFED.

## Slide 14: SRP Command Request

## Slide 15: iSER
iSER

## Slide 16: iSER (iSCSI Extensions for RDMA)
iSER leverages on iSCSI management and discovery
  Zero-Configuration, global storage naming (SLP, iSNS)
  Change Notifications and active monitoring of devices and initiators
  High-Availability, and 3 levels of automated recovery
  Multi-Pathing and storage aggregation
  Industry standard management interfaces (MIB)
  3rd party storage managers
  Security (Partitioning, Authentication, central login control, ..)
Working with iSER over IB Doesn’t require changes !!!
  Enable investment protection (software, education, training, ..)
  Reduce the fear-factor of IB

## Slide 17: iSCSI Mapping to iSER
iSCSI Mapping to iSER / RDMA Transport
iSER eliminates the traditional iSCSI/TCP bottlenecks :
  Zero copy using RDMA
  CRC calculated by hardware
  Work with message boundaries instead of streams
  Transport protocol implemented in hardware (minimal CPU cycles per IO)
BHS
AHS
HD
Data
DD
Protocol frames (RDMA)
iSCSI PDU
RC Send
RC RDMA Read/Write
X
In HW
X
In HW

## Slide 18: iSER Protocol (Read)
SCSI Reads
  Initiator Send Command PDU (Protocol data unit) to Target
  Target return data using RDMA Write
  Target send Response PDU back when completed transaction
  Initiator receives Response and complete SCSI operation
iSCSI Initiator
iSER
HCA
HCA
iSER Target
Target Storage
Send_Control (SCSI Read Cmd)
RDMA Write for Data
Send_Control + Buffer advertisement
Control_Notify
Data_Put (Data-In PDU) for Read
Control_Notify
Send_Control (SCSI Response)

## Slide 19: iSCSI Discovery-Direct SLP
Client Broadcast: I’m xx where is my storage ?
FC Routers discover FC SAN
Relevant iSCSI Targets & FC gateways respond
Client may record multiple possible targets & Portals
GbE Switch
FC Switch
IB to IP Router
Native IB RAID
IB to FC Routers
iSCSI Client
Portal – a network end-point (IP+port), indicating a path

## Slide 20: iSCSI Discovery-iSNS
FC Routers discover FC SAN
iSCSI Targets & FC gateways report to iSNS Server
Client ask iSNS Server: I’m xx where is my storage ?
iSNS responds with targets and portals
resources may be divided to domains
Changes notified immediately (SCNs)
GbE Switch
FC Switch
IB to IP Router
Native IB RAID
IB to FC Routers
iSCSI Client
iSNS or SLP run over IPoIB or GbE, and can span both networks
iSNS Server

## Slide 21: Conclusion
Both SRP and iSER support RDMA
  Source and Destination Addresses in the SCSI transfer
  Zero memory copy
SRP Uses
  Direct server connections
  Small controlled environments
iSER Uses
  Large switch connected Networks
  Discovery fully supported

## Slide 22
Adventures Installing Infiniband Storage
Randy Kreiser Chief Architect
Sonoma OpenFabrics Workshop 1 May 2007
Notes: <number>