## Slide 1: Uncovering Performance and Interoperability Issues in the OFED Stack March 2008
Dennis Tolstenko
Sonoma Workshop Presentation
Notes: <number>

## Slide 2: Agenda
Agent Overview
Functionality
Uses
Demo

## Slide 3: RDMA Agent Overview
The RDMA Agent is a simple application that resides on a host running OFED.
Requires no hardware and is installed via an rpm
Runs as a daemon or can be manually started/stopped
Uses an out of band control interface which allows centralized management and control of the following:
  Discovery of RDMA Hosts
  Establishing RDMA DATA Channels
  Generating RDMA Reads, Writes, and Sends
  Gathering Performance results, validating interoperability and detecting errors.
Notes: <number>

## Slide 4: RDMA OFA Agent Diagram
Client Application
RDMA Test Agent
OFA Software Stack
RDMA Host
RDMA Test Agent
OFA Software Stack
RDMA Host
RDMA Data Channel
TCP/IP Control Channel
TCP/IP Control Channel
Notes: <number>

## Slide 5: Control Interface
The out of band control interface is implemented using a simple protocol named PULP.
PULP fills the role of the Application layer.
It allows a client to define a set of operations which can be presented to the control component of the DUT.
It is a “command-response” protocol.
Notes: <number>

## Slide 6: Control Channel
Control Channel is the conduit for PULP requests and responses.
The Control Channel is instantiated via a TCP/IP connection
Multiple control channels can be established for parallel processing.
The application supports unsolicited message passing.
Notes: <number>

## Slide 7: Agent Discovery
RDMA Agents are discoverable via a UDP broadcast messages.
The Discover Response contains the following information:
  Host Information:
    Host Name and IP address
    Host OS and Kernel
    OFED version
  A list of RDMA Interfaces:
    IP Address
    Interface Name
    Status of the Link
    Vendor name
    SW Version
    HW Version
Notes: <number>

## Slide 8: RDMA Traffic
The RDMA Agent allows the user to define & execute the following RDMA Operations:
  RDMA READ
  RDMA Write
  RDMA SEND
Each RDMA Operation has the following fields:
  Size – Number of bytes to transfer
  Count – Number of RDMA operations to send
  Delay – ms between each operation
Features
  Run RDMA Operations serially (allows for ordering)
  Run RDMA Operations in parallel on one or more Data Channels
  Traffic shaping can be achieved through Size, Count and Delay
Notes: <number>

## Slide 9: Gathering Results
Each RDMA Completions contains:
  RDMA Operation Type (Send, Read, Write)
  Total bytes Transferred
  Number of RDMA executions
  Time taken to complete
  Completion Status
  Error Number
  Vendor Error Number
Calculated values
  Application Throughput
  Rate Of Operations
Notes: <number>

## Slide 10: Agent Highlights
Centralized management and control
Fabric Discovery & RDMA Device information
Able to define and generate RDMA Read, Write and Sends.
Accurate performance measurement
Notes: <number>

## Slide 11: RDMA Agent Solutions
Simplify interoperability testing
Stress test RDMA Devices with the OFED stack
Measure true performance at the Application Layer
Provide a mechanism to test IB Verbs
Active Compliance Testing
Notes: <number>

## Slide 12: XANStorm Overview
XANStorm is the first application to use the RDMA OFA Agent.
Easy to use intuitive GUI
Works for both InfiniBand and iWARP
Works on Linux or Windows

## Slide 13: XANStorm Key Features
Fabric Discovery and Topology Configuration
Interoperability Testing
Performance Measuring
Stress Testing
Automated Regression Testing
Clear, Easy to Read Results
No Additional Hardware Needed

## Slide 14: Discovery
  Discover all nodes on the cluster (IB and iWARP)
  Provides a detailed information on each RDMA Host.
  Create single or multiple connections between two or more nodes in the fabric
  Manual control available for custom configuration

## Slide 15: RDMA Operations
Define Sequence of RDMA Operations
Testing options
  RDMA Type
  Data Size
  # of RDMA Operations to execute
  timing (traffic shaping) of operations
  direction of traffic flow between nodes
  number of connections between nodes

## Slide 16: Comprehensive Results
  Results from running the “Performance Seq”
  Results are gathered & presented in real time

## Slide 17: Agent and XANStorm Information
See an online presentation 24/7
  www.lampreynetworks.com/xanstorm_demo
Request Demo product
  http://www.lampreynetworks.com/Content/iWARP/iWARP_RDMAgenerator.html
LNI sales contacts
  (603) 868-8411
  sales@lampreynetworks.com