## Slide 1: OFED 1.3
April 2008
Tziporet Koren
Notes: <number>

## Slide 2: Agenda
OFED 1.3
OFED 1.3.x releases

## Slide 3: OFED 1.3 – General Info
Released on Feb 28
Distros integration:
  RH AS 4.7 and RHEL 5.2
  SLES10 SP2
Passed OFA interop on March

## Slide 4: OFED 1.3 Components
HCA/NIC Drivers
  IB: IBM, Mellanox, QLogic
  iWARP: Chelsio, NetEffect
Core: verbs, mad, SMA, CMA, SA cache
IPoIB
SDP
SRP
iSER
SRP Target
RDS
Qlogic_VNIC
UDAPL
OSM
Diagnostic tools
Bonding module
Open iSCSI
MPI Components
  MVAPICH
  Open MPI
  MVAPICH2
  Benchmark tests
Proprietary MPIs: Intel, HP, Scali
Proprietary SMs: Cisco, Voltaire, Qlogic
OFA development
Add on
Tested with

## Slide 5: Main Benefits of OFED 1.3
Improved performance, scalability and latency across networks
Simplifies and accelerates the deployment of InfiniBand and iWARP solutions, by ease on distros OFED integration
Quality of Service (QoS) management capabilities that enable unified LAN, IPC and SAN applications over the same wire
New routing algorithms to help optimize network and system performance and scalability
Improved upper layer protocols for superior IP and sockets-based application performance, including database applications
Enhancements that enable MPI and applications to scale efficiently to large numbers of nodes while reducing the memory footprint required on servers
Enhanced diagnostic tools to improve network management
Support for additional Independent Hardware Vendor (IHV) solutions
Expanded interoperability with OEM solutions, including network and storage equipment, to provide enterprise IT departments with more flexibility

## Slide 6: Details on Main New Features
Base kernel: 2.6.24
Install
  Minimize integration effort into OS distribution
  User level split into separately-installable RPMs
  Based on feedback from Novell and Redhat
Package
  Sources arrangement for the end user
  Added the make-dist script
Reduce compilation warnings of backports

## Slide 7: New Features – Cont.
QoS
  OSM, CM & CMA, ULPs: SRP, SDP, iSER, IPoIB, RDS, MPI
Updated SA cache
  Integrated with sa_query module
  Use of SA events (GID up/down) to provide additional synchronization
  User-space control for dynamic enable/disable and update
Extended RC (XRC) Support
  New verbs to enable XRC
New modules
  NES (NetEffect driver)
  SRP Target: Based on Mellanox IBGD SRPT and interfaces with SCST scsi target middle level driver

## Slide 8: Main New Features – ULPs
IPoIB
  NAPI
  Stateless offloads (checksum, scatter/gather, LSO) – for Datagram mode
  Small message performance improvements
  Non-SRQ for the CM
  4K MTU
  Interrupt moderation (can be configured with ethtool)
RDS:
  RDMA with Zero copy (API version 3)
  GA of Send copy (API version 2)
SDP:
  Send Zero Copy
  Asynch IO
  Keep alive
uDAPL 2.0
  In addition to uDAPL 1.0

## Slide 9: Main New Features – Management
OpenSM
  Quality of Service manager
    QoS implementation of the IBTA annex
    QoS policy parser and support for SA (PR, MPR)
  Scalability/stability improvements
    Performance improvements of the routing algorithms (min-hops, up/down, lash)
    Optimized port and switch tables update policy
  “Native” daemon mode
Performance manager
  Fetches and stores performance counters
  OpenSM integrated, work in any OpenSM state (standby, disabled)
  Plug-in interface
Diagnostic tools enhancements
IBSIM – IB fabric simulator (new)
  Emulates user_mad layer
  useful for OpenSM and management tools testing

## Slide 10: Main New Features - MPI
MVAPICH 1.0
  Asynchronous progress
  Flexible message coalescing
  APM support
  Enhanced mpirun_rsh for scalable launching
  UD-based design
  Optimized and tuned collectives
  Support for ConnectX
  Support for QLogic/PSM
Open MPI 1.2.5
  ConnectX support
MVAPICH2 1.0
  Message Coalescing
  Hot-spot avoidance
  Application-initiated systems-level checkpointing
  APM support
  Multi-rail support for iWARP
  On-demand connection management for iWARP and uDAPL
  RDMA Read
  Blocking

## Slide 11: OFED 1.3 OS Matrix
kernel.org: kernel 2.6.23 and 2.6.24
Novell
  SLES 10
  SLES 10 SP1 (up1)
Redhat
  RHEL 4 (up4, up5, up6)
  RHEL 5 (up1)
Free distros (partial support only; no QA):
  Open SuSE 10.3
  Fedore C6 & C8
  Ubuntu 6.06 (with RPM package installed)

## Slide 12: Release Plan vs. Actual
Original schedule (SC07)
  Features freeze: Oct 10, 07
  Alpha: Oct 15, 07
    kernel 2.6.23
  Beta: Nov 20, 07
    kernel 2.6.24-rc2
  RC1: Dec 4, 07
  RC2: Dec 18, 07
  RC3: Jan 8, 08
  RC4: Jan 22, 08
  GA: Jan 29, 08
Actual Schedule
  Features freeze: Oct 10, 07
    Was not a real freeze
  Alpha: Oct 15, 07
    kernel 2.6.23
  Beta: Nov 22, 07
    kernel 2.6.24-rc2
  RC1: Dec 13, 07
  RC2: Jan 16, 08
  RC3: Jan 30, 08
  RC4: Feb 07, 08
  RC5: Feb 21, 08
  RC6: Feb 25, 08
  GA: Feb 28 08

## Slide 13: OFED 1.3.x Releases
1.3.1 is planed for May 29
  Critical bug fixes in:
    IB-bonding
    SRP failover
    SDP crashes
    RDS fixes for RDMA API
  Low level drivers:
    nes
    mlx4
    cxgb3
    Ipath
    ehca
  librdmacm 1.0.7
Will do more maintenance releases if needed

## Slide 14: Thank You