## Slide 1
Driver Mapped Memory Memory Pinning I/O to process address space Access of address spaces across Linux Instances
Christoph Lameter, Ph.D.
Principal Engineer, Linux Kernel Software
Silicon Graphics, Inc.
clameter@sgi.com
2008-04-07
OpenFabrics Forum

## Slide 2: Memory Pinning under Linux
Ensure that memory subject to device access does not go away.
External References vs. Linux Native References
  OS looses control over memory
  Reclaim issues
Users
  Device I/O directly to user mapped pages (RDMA).
  DMA engines (Intel, GRU, network).
  Virtualization (host <-> guest, guest <-> guest)‏
  Inter Linux Shared Memory (SHMEM, XPMEM..)‏

## Slide 3: The problem
Device Page tables not managed by the VM
Device TLBs not managed by the processor
Mappings by other Linux instances
Pages must not vanish while mapped by TLBs, Page tables, devices or other things
VM assumes that it is in control of memory and that all of memory is reclaimable.
Problems for page reclaim, dirty throttling etc.
Cycling through LRU lists may lead to livelocks.

## Slide 4: Pinning using mlock()‏
Available from user space. VM knows which address spaces have mlocked pages.
Posix definition of mlock(): Pages must not be swapped out (this is the accepted meaning of mlock for Linux).
But can be moved by
  Memory Hotplug
  Page migration (NUMA only)‏
  Defragmentation (not implemented yet)‏
Mlock is unlimited! Yay!
Not inherited via exec.
Pages may vanish when the mlock'ing process vanishes.

## Slide 5: Pinning by increasing refcount
Refcount is obtained via get_page()‏
VM unable to unmap page.
VM does not know that the page is pinned(!)‏
Refcounts are taken temporarily or due to processes mapping pages.
Pages survive even after all processes terminate.
Device must actively decrement refcount and free page (put_page()). This means tracking the pinned pages.

## Slide 6: Solutions
Make the VM account mlocked pages and adjust reclaim accordingly (creates new LRU list, more complex reclaim logic).
Add a way to mark pinned pages. Then do the same as above.
Solutions mean that VM looses control over memory. Drivers can arbitrarily reduce memory available to the OS.
Another solution: Cooperation between drivers that want stable memory references and the OS. VM can evict memory if needed by making the device remove the references. VM can use facility to provide full support (reclaim, page migration, hotplug, remapping) for those areas.

## Slide 7: Externally Mapped Memory Notifier (EMM) or MMU notifier
A device driver subscribes to an address space for callbacks (emm_register())‏
Device driver establishes references to pages as needed (may increment refcount or not).
Callback emm_notify(struct mm_struct *, operation, from, to).
VM will only remove references between emm_invalidate_start / emm_invalidate_end callbacks. The device can take appropriate actions.
Subscription is terminated when the process terminates (emm_release).

## Slide 8: Notifier API
enum emm_operation {
emm_release, /* Process is exiting. Drop driver resources */
emm_invalidate_start, /* Before the VM unmaps pages. Forbid new refs */
emm_invalidate_end, /* After the VM unmapped pages. Allow new refs */
emm_referenced, /* Return number of times range was referenced */
};
struct emm_notifier {
int (*callback)(struct emm_notifier *e, struct mm_struct *mm,
enum emm_operation op, unsigned long start, unsigned long end);
struct emm_notifier *next;
};
/*
* Register a notifier with an mm struct. Release occurs when the process
* terminates by calling the notifier function with emm_release.
*/
extern void emm_notifier_register(struct emm_notifier *e, struct mm_struct *mm);

## Slide 9: Notifier user that does not increment the refcount
The page can be freed between emm_invalidate_start and emm_invalidate_end as soon as the VM unmaps the page.
Driver does not need to keep state of which pages are mapped (important for TLB page references with simple shoot down semantics)‏
Driver can use follow_page() from interrupt context.
Hardware TLB synchronization can be used to avoid having to use locks in the driver.
emm_invalidate_start simply zaps all the TLBs in a range and forbids new refs to be established.
emm_invalidate_end re-enables new references.

## Slide 10: Notifier user that increments page refcount
Driver does an additional or implied get_page() when the page is mapped to a process
Requires the use of get_user_pages().
Page can only be removed when the driver drops the refcount.
emm_invalidate_start: Forbid new references (optionally drop references and page refcount).
emm_invalidate_end: Drops reference of pages were refcount was taken which may free them.
Pages may continue to exist even after VM has unmapped them from the process until the device driver drops refcount.

## Slide 11: Relevant Projects
MMU Notifier / EMM notifier
Removal of Mlocked pages and unreclaimable pages from page reclaim (Nick Piggin, Lee Schermerhorn, Rik van Riel and me).
Adding of support for pinned pages in the VM to recognize that they are not reclaimable (Lee Schermerhorn and me).