## Slide 1: Fibre Channel over InfiniBand
Dror Goldenberg Mellanox Technologies

## Slide 2: Agenda
Background and Motivation
Protocol Overview
Software Stack Architecture

## Slide 3: I/O Consolidation
Connect islands of IB to network and storage fabrics
Key factors
  Gateways
    Cost, performance, scalability, simplicity
  Management
Converge
with InfiniBand
OS
Storage App
Network App
Manage- ment App
OS
Network App
Manage- ment App
IB HCA
Storage App
One wire
GbE NIC
GbE NIC
FC HBA
Notes: We’ve seen that InfiniBand is the best fabric solution for Storage Area Networking. It is also the only fabric that fully enables I/O consolidation and allow customers to use a single wire for networking, clustering and storage traffic and allows the Quality of service for each traffic type to be determined and managed.

## Slide 4: Why FCoIB ?
Management
  Similar to Fibre Channel
Transparency to applications
  FC software runs over IB wires
  Similar frame format / protocol
  Similar driver infrastructure
Gateways - complexity reduction
  SCSI transport termination  stateless packet relay
  Better performance/scalability at lower cost
Better support for legacy storage attachment
Gateway
Host
Fibre Channel
Host
Host
InfiniBand

## Slide 5: FC over IB Gateway Model
NPIV N_Ports
FC Begins Here
Physical View:
Handling initiators logins
Acts as an NPIV N_Port
  Reflects F_LOGI as F_DISC
Virtualized
Server
Logical View:
NPIV HBA
Fibre Channel
Host
Host
Host
FCoIB to FC Gateway
Fibre Channel
InfiniBand
“PCIe
extension”

## Slide 6: FCoIB Gateway – Stateless Packet Relay
IB to FC
  Strip IB headers
    Payload contains entire FC frame
FC to IB
  D_ID lookup to retrieve addressing {LID, QPN, etc.}
  Encapsulate FC frame as UD payload
IB CRC
IB Headers
FC Frame
FC Frame
IB CRC
IB Headers
FC Frame
FC Frame
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: FCoIB Protocol
Encapsulation of Fibre Channel frames over IB transport
  FC-0 Physical is replaced by IB Physical
  FC-1 Encode/Decode, Framing and Link Control are replaced by IB link and framing
    Degenerated delimiters are encapsulated
      Similar to FCIP/iFCP RFC 3821/4172
    Routing according to IB addresses (LID/GID/QP)
  FC-2 and above remain intact
Similar concept to IP over IB encapsulation (RFC 4391)
  FCoIB HBA is an IB UD application

## Slide 8: Frame Encapsulation
Encapsulated FC Frame
VCRC
DETH
LRH
DestQP field indicates FC
FC Payload
(0 to 2112 bytes)
FC Header
(24 bytes)
Enc. SOF
(4 bytes)
FC CRC
(4 bytes)
Enc. EOF
(4 bytes)
Destination QP indicates FC Nx_Port
  FCoIB HBA is an IB UD application
Gateway maintains mapping between FCID and IB address
ICRC
BTH
IB Headers
IB CRCs

## Slide 9: Discovery
Identifying the Gateway
  Through an IB specific mechanism (TBD)
    e.g. Service Record, IO Controller, Multicast
  Results in {GID,QPN} of the gateway
FLOGI between IB initiator and the gateway
  Gateway initiates an F_DISC with the fabric
Other frames can be relayed intact

## Slide 10: Software Stack Architecture
Open FC
mlx4_en
TCP/IP
SCSI midlayer
mlx4_core
mlx4_ib
IB Core
mlx4_fc
IB Client (Discovery)
send() - non offloaded
scsi_send() - offloaded I/O

## Slide 11: mlx4_fc HW Interface
FC Raw Frame Interface (RFCI)
  Sends and receives FCoIB frames
  FC CRC offload
FC Command Queues (FCMND)
  Initiate IO operation
  Owns bulk of FEXCH Queues
FC Exchange Queues (FEXCH)
  Data transfer
  Statically allocated to FCMND queues
  Pre allocated chunk of queues
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: mlx4_fc HW Interface
FC Memory Keys
  Single/dual MKey per FEXCH
    Pre-allocated chunk of Data MKeys
  Used to register buffers for IOP
  Zero Copy Operations
Completions, Events, Interrupts, Command interface
  As usual
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: mlx4_core
Resource broker
  Allocation of chunks of QPs/MRs to upper drivers
Command interface serialization

## Slide 14: Example IO Read Flow
FCP_CMND
FCP_DATA
FCP_RSP
IORead CMD
Allocate xChg
Map DMA Area
Register memory
Issue CMD
openfc
mlx4_fc
Zero Copy
HW DMA
Response
IB wire
ConnectX
IO Read Done
Release xChg
Unmap DMA

## Slide 15: Summary
FCoIB – FC frames Encapsulation over IB UD
  FCoIB is a UD application
Simplifies gateway implementation
  Performance, cost, scalability
Simplifies software and management
  FC look & feel
Protocol is fully offloaded in ConnectX