## Slide 1: Quality and Service in OFED 3.1
Liran Liss
Mellanox Technologies Inc.

## Slide 2: Agenda
QoS motivation
InfiniBand QoS overview
Host software support
  IB stack
  ULPs
QoS manager
  Programming QoS levels in the fabric
  Configuring a QoS policy
Example configurations
Future work

## Slide 3: QoS Motivation
Multiple data-center traffic types
Each requires different service properties
  BW
  Latency
  Reliability
QoS achieves these requirements on a unified wire
Administrator
Storage
IPC
IB-Ethernet Gateway
QoS Manager
Servers
Filer
Block Storage
InfiniBand Subnet
Net.
IB-Fibre Channel Gateway
Unified I/O
Notes: All sorts of traffic; different needs, need to provide these needs in a single fabric

## Slide 4: QoS in Infiniband – Overview
Infiniband fabrics support up to 15 Virtual Lanes (VLs) for data
  Each virtual lane has dedicated resources
  Virtual lanes are arbitrated at each host/switch using a dual-priority Weighted Round Robin (WRR) scheme
Flows are classified into Service Levels (SLs) at end nodes
  Each packet sent is marked with the corresponding SL
  Packets are mapped to VLs in each link according to their SL
High Priority
WRR
Low Priority
WRR
Priority
Select
Packets
to be
Transmitted
H/L Weighted Round Robin (WRR) VL Arbitration
Notes: ConnectX: 8 + vl15?
VLs can be configured \\

## Slide 5: QoS in Infiniband (IB spec v1.2.1- A13)
Administrator configures fabric
  Fabric QoS levels
    SL-to-VL mappings
    High/low VL arbitration
  QoS policy
Applications send PathRecord queries to SA
  May also include additonal QoS fields
    ServiceID, QoSClass
SA consults QoS manager before replying
  In Active QoS Management: fabric may be dynamically reconfigured
Applications use PathRecord fields for sending traffic
Fabric enforces QoS accordingly
SM, SA, and QoS man. Implemented by opensm
Can also be reconfigured at runtime

## Slide 6: QoS in Infiniband (IB spec v1.2.1- A13)
Administrator configures fabric
  Fabric QoS levels
    SL-to-VL mappings
    High/low VL arbitration
  QoS policy
Applications send PathRecord queries to SA
  May also include additonal QoS fields
    ServiceID, QoSClass
SA consults QoS manager before replying
  In Active QoS Management: fabric may be dynamically reconfigured
Clients use PathRecord fields for sending traffic
Fabric enforces QoS accordingly
SM, SA, and QoS man. Implemented by opensm
We will start with this…
…to know how to do this
Can also be reconfigured at runtime

## Slide 7: QoS in IB Stack
SA Client
  Fills in QoS related components
    Pkey, QoS-class, Traffic class, ServiceID
  Interpretation left to QoS manager (opensm)
    Returns desired SL, MTU, rate, packet-life time, etc.
RDMA CM
  Transport neutral interface
  Uses ServiceID, QoS class, and Traffic Class in path queries
    ServiceID is port-space prefix + port
    QoS class used for IPv4 – ToS value from ‘rdma_set_service_type()’
    Traffic class used for IPv6 – taken from sockaddr_in6 address
Notes: “multi-cast already support traffic class” !#????
IPv4 TOS, IPv6 TC,  diffserve code point
Set_service_type – before address resolution, only affects new connections…

## Slide 8: QoS in ULPs
SRP
  Based on target port GUID (ServiceID is currently vendor specific)
IPoIB
  Based on global multicast group settings
  Provides Pkey in each path resolution
SDP
  Uses RDMA CM service – provides ServiceID
iSER
  Uses RDMA CM service – provides ServiceID
RDS
  Uses RDMA CM service – provides ServiceID
MPI
  Currently does not issue PathRecord queries (SM integration planned)
    Uses SL given at command line directly and exchanges LIDs via TCP
Notes: Traffic class for IPoIB – good only for QoS based on connected nodes, not flows, etc.
*** Does IPoIB take the SL from the pkey

## Slide 9: SM Configuration
Relevant configuration files
  Partitions (/etc/ofa/opensm-partitions.conf)
  SL/VL tables (/var/cache/opensm/opensm.opts)
  QoS policy (/etc/ofa/opensm-qos-policy.conf)

## Slide 10: Configuring SL-to-VL and VL Arbitration
Weights are specified in 64 byte credits
  Use multiples of MTU/64 (e.g., 32 for 2K MTU)
  VLs with 0 credits are never scheduled
  Special high-limit values: 0 – single packet, 255 – no limit
Device specific configuration
  CA (_ca_), router (_rtr_), switch port 0 (_sw0), switch external ports (_swe_)
# QoS default options
qos_max_vls 15
qos_high_limit 0
qos_vlarb_high 0:32,1:0,2:0,3:0,4:0,5:0,6:0,7:0,8:0,9:0,10:0,11:0,12:0,13:0,14:0
qos_vlarb_low 0:0,1:32,2:32,3:32,4:32,5:32,6:32,7:32,8:32,9:32,10:32,11:32,12:32,13:32,14:32
qos_sl2vl 0,1,2,3,4,5,6,7,8,9,10,11,12,13,14,7
# QoS CA options
qos_ca_max_vls 15
qos_ca_high_limit 0
qos_ca_vlarb_high 0:32,1:0,2:0,3:0,4:0,5:0,6:0,7:0,8:0,9:0,10:0,11:0,12:0,13:0,14:0
qos_ca_vlarb_low 0:0,1:32,2:32,3:32,4:32,5:32,6:32,7:32,8:32,9:32,10:32,11:32,12:32,13:32,14:32
qos_ca_sl2vl 0,1,2,3,4,5,6,7,8,9,10,11,12,13,14,7

## Slide 11: QoS Policy Configuration
File consists of the following optional sections:
  qos-ulps
  port-groups
  qos-levels
  qos-match-rules
Two configuration models
  Simplified
    Only qos-ulps section required
  Advanced
Advanced model takes precedence

## Slide 12: Simple QoS Policy
Assigns SLs according to:
  IPoIB with default / specified pkey
  SDP / iSER / RDS with (optional) port ranges
  SRP with target port guid
  Any application with specific ServiceId / pkey / target port guid range
First rule takes precedence
qos-ulps
sdp, port-num 10000-20000 : 2
sdp : 0
srp, target-port-guid 0x100000000000FFFF : 4
rds, port-num 25000 : 2
rds : 0
iser : 4
ipoib, pkey 0x0001 : 5
ipoib : 6
any, pkey 0x0ABC : 3
default : 0
end-qos-ulps
Notes: Order counts – ipoib traffic to the SRP target port will be caught be SRP rule
Default must be defined – place doesn’t matter

## Slide 13: Advanced QoS Policy
Define port groups
Define QoS levels
  A level specifies requirements for SL, MTU, rate, etc.
Define matching rules that map PathRecord components to QoS levels
  Uses port groups and partition names to facilitate syntax

## Slide 14: Advanced QoS Policy – port groups
Defined based on
  GUID
  Node description/port
  Partition names
  PKeys
  Type (CA/Switch/etc.)
Identified by ‘name’ field
  ‘use’ field is for logging only
port-groups
port-group
name: Storage
use: SRP storage targets
port-guid: 0x100000000000FFFF
port-guid: 0x100000000000FFFA
end-port-group
port-group
name: Virtual Servers
use: node desc and IB port num
port-name: ws1 HCA-1/P1, ws2 HCA-1/P1
end-port-group
port-group
name: Engineering
partition: Part1
pkey: 0x1234
end-port-group
port-group
name: Switches and SM
node-type: SWITCH, SELF
end-port-group
end-port-groups

## Slide 15: Advanced QoS Policy – QoS Level
Level = subset of PathRecord attributes
  SL, MTU, Rate, packet-life
  Uses standard PathRecord encoding
Identified by ‘name’ field
  ‘use’ field is for logging only
qos-levels
qos-level
name: DEFAULT
use: default QoS Level
sl: 0
end-qos-level
qos-level
name: Low Priority
use: for the lowest prio
sl: 14
end-qos-level
qos-level
name: WholeSet
sl: 1
mtu-limit: 4
rate-limit: 5
packet-life: 4
end-qos-level
end-qos-levels

## Slide 16: Advanced QoS Policy – Matching Rules
qos-match-rules
qos-match-rule
use: by class 7-9 or 11
qos-class: 7-9,11
qos-level-name: WholeSet
end-qos-match-rule
qos-match-rule
use: Storage targets
destination: Storage
service-id: 22,4719-5000
qos-level-name: DEFAULT
end-qos-match-rule
qos-match-rule
use: match by all parameters (AND)
qos-class: 7-9,11
source: Virtual Servers
destination: Storage
service-id: 22,4719-5000
pkey: 0x0F00-0x0FFF
qos-level-name: WholeSet
end-qos-match-rule
end-qos-match-rules
A rule maps a subset of
  Class
  Source port group
  Destination port group
  Service ID
  Pkey
to a QoS level
First matched rule wins
Notes: Can we add multiple range lists? Can we use hex/base10 freely?

## Slide 17: Usecase 1: HPC
QoS Levels
  MPI
    Separate from I/O load
    Min BW of 70%
  Storage Control (Lustre MDS)
    Low latency
  Storage Data (Lustre OST)
    Min BW 30%

## Slide 18: HPC QoS Administration
MPI
  mpirun –sl 0
OpenSM
  QoS policy file:
  Options file:
qos-ulps
default :0 # default SL (for MPI)
any, target-port-guid OST1,OST2,OST3,OST4 :1 # SL for Lustre OST
any, target-port-guid MDS1,MDS2 :2 # SL for Lustre MDS
end-qos-ulps
qos_max_vls=8
qos_high_limit=0
qos_vlarb_high=2:1
qos_vlarb_low=0:224,1:96
qos_sl2vl=0,1,2,3,4,5,6,7,15,15,15,15,15,15,15,15

## Slide 19: Usecase 2: EDC
QoS Levels
  Management traffic (ssh)
    IPoIB management VLAN (partition A)
    Min BW 10%
  Application traffic
    IPoIB application VLAN (partition B)
    Isolated from storage and database
    Min BW of 30%
  Database Cluster traffic
    RDS
    Min BW of 30%
  SRP
    Min BW 30%
    Bottle neck at storage nodes

## Slide 20: EDC QoS Administration
OpenSM
  QoS policy file
  Options file
  Partition configuration file
qos-ulps
default : 0
ipoib, pkey 0x8001 : 1
ipoib, pkey 0x8002 : 2
rds : 3
srp, target-port-guid SRP1, SRP2, SRP3 : 4
end-qos-ulps
qos_max_vls=8
qos_high_limit=0
qos_vlarb_high=1:32,2:96,3:96,4:96
qos_vlarb_low=0:1,
qos_sl2vl=0,1,2,3,4,5,6,7,15,15,15,15,15,15,15,15
Default=0x7fff,ipoib: ALL=full;
PartA=0x8001, sl=1, ipoib: ALL=full;
PartB=0x8002, sl=2, ipoib: ALL=full;
Notes: SLs in unicast IPoIB do not find their way to mcast group
Why do we need to asign SL to partitions???

## Slide 21: Future Work
Configuration file organization
  Move port groups to a different file
    Used both by partition and QoS files
  Move SL/VL configuration to QoS file
  Remove QoS options from partition file
    These will be obtained by IPoIB from MGID PathRecord
Add wildcards for port-name matching
Provide “user friendly” aliases to SA attribute encodings (e.g., MTU256)
Add Traffic Class to matching rules
Extend host-side QoS
  BW limiting
  WRR scheduling between QP groups sharing the same SL

## Slide 22: Summary
QoS in Infiniband is simple and elegant
  Centrally managed, consistent throughout the fabric
Fully functional in OFED1.3
  All ULPs are QoS aware
  QoS manager integrated in opensm
Configuration is a piece of cake
  Just assign each ULP the desired service level

## Slide 23
Thank You !