## Slide 1: Open MPI OpenFabrics Update
April 2008
Jeff Squyres

## Slide 2: Sidenote: MPI Forum
MPI Forum re-convening
  2.1: bug fixes, consolidate to one document
  2.2: “bigger” bug fixes
  3.0: addition of entirely new stuff
Strongly encourage all to participate
  Hardware / MPI vendors
  ISVs who use MPI
  MPI end users
Next meeting: April 28-30, Chicago

## Slide 3: OMPI Current Membership
15 members, 9 contributors, 1 partner
  6 research labs
  8 universities
  10 vendors
  1 individual

## Slide 4: Current Status
Stable release series: 1.2
  Current community release: v1.2.6
    Released yesterday
    Bug fix release
  OFED v1.3 includes: v1.2.5
    Will include v1.2.6 in OFED v1.3.1
Working towards next major series: 1.3
  Exact release date difficult to predict
  “Herding the cats”

## Slide 5: v1.3: OpenFabrics Features
Connection Manager support
  IB CM (many thanks Sean Hefty), RDMA CM
XRC support
APM support
BSRQ (including XRC integration)
  Multiple receive queues with different size buffers (i.e., send on Q with closest size)
  More efficient use of registered memory
No use of UD [yet?]

## Slide 6: New iWARP Support
Open Grid Computing / Chelsio
  Adding RDMA CM, auditing verbs usage
More difficult than initially expected
  Adding CM support to OMPI was “hard”
  Many firmware, driver, and OMPI bugs
Work mostly complete; still to-do:
  Init parameter file extensions
  Multiple ports / devices striping setup

## Slide 7: iWARP Challenges
Chelsio T3 does not support SRQ
ibv_post_recv() race condition
  OMPI uses multiple QPs per peer pair (BSRQ)
  But all OMPI flow control goes on one QP
Registered memory utilization will be poor
  Both issues fixed in “T4”
Connection “initiator-must-send-first” issue
  Solved by hiding 0 byte RDMA read in Chelsio firmware / driver (NetEffect has similar)
  More general / NIC-independent solution coming in OFED 1.4

## Slide 8: iWARP Lessons Learned
No “huge” surprises
  Verbs worked as expected
Open MPI and MVAPICH use the verbs stack very differently
  Brought out many, many latent vendor bugs
  Strongly encourage other iWARP vendors to start testing / participating ASAP
MPI Testing Tool (MTT) can help!

## Slide 9: Other v1.3 Features
Dropping VAPI support
Major job launch scalability improvements
  LANL RoadRunner (LANL, IBM)
  TACC Ranger (Sun)
  Jaguar (ORNL)
Tighter integration with parallel tools
  DDT parallel debugger “understands” opaque MPI handles
  VampirTrace integration (tracefile / post-mortem analysis)

## Slide 10: Other v1.3 Features
“Manycore” issues
  Use newest Portable Linux Processor Affinity (PLPA) release (see www.open-mpi.org)
  Allow binding to specific socket/core
  “Better” integration to resource managers to allow them to handle affinity (post 1.3?)
First cut of “Carto”[graphy] framework
  Discover and use topology of host, fabric
  Port selection, collective algorithms

## Slide 11: Roadmap
1.3 release taking too long
  Group decided 1.3 feature-driven, not time
  About 1.5 years since initial 1.2 release
May move to a shorter plan release cycle
  At least once a year?
  Still under debate
Have a variety of features planned for “post 1.3” releases

## Slide 12: Come Join Us!
http://www.open-mpi.org/