## Slide 1: STGT/iSER Target Overview
Or Gerlitz
Voltaire
ogerlitz@voltaire.com

## Slide 2: agenda
some background
general structure / architecture
target drivers
  iSCSI target & iSCSI RDMA (iSER) transport
SCSI devices
using / configuring STGT
some performance numbers
STGT community

## Slide 3: some background
framework for SCSI protocol independent target
open source
STGT implemented / maintained by Fujita Tomonori & Mike Christie
iSCSI RDMA (iSER) transport implemented by Ohio Supercomputer Center staff under the direction of Pete Wyckoff

## Slide 4: general structure / architecture
The architecture is made of three elements:
1st : the SCSI state machine, I/O execution and management interface which are:
  done in a SCSI protocol independent manner
  pushed to user space, executed by tgtd user space daemon
2nd : target drivers - network interface
3rd : SCSI devices - storage interface
the Linux kernel was enhanced (2.6.20) to allow STGT use kernel target drivers

## Slide 5: target drivers
user space – iSCSI, FCoE
kernel space – FC, IBMVIO
target driver API to tgt core
  target create / destroy / update / show
  lu create / lun get
  notify on end of command / management

## Slide 6: iSCSI target driver
has iSCSI transport independent state-machine
utilizes iSCSI transport “library”
current transports: TCP and RDMA (iSER)
iSCSI transport API to the iSCSI target driver
  uses “end-point” notation to describe a connection
  end-point read / write / rdma-read / rdma-write
  end-point (implicit accept) / close / release / show
  data buf alloc / free

## Slide 7: iSCSI RDMA (iSER) transport
implemented over libibverbs and librdmacm
  direct access to the RDMA HW device
  RDMA transport neutral*, adopted to the Linux initiator
data transfer
  uses RC QP (Queue Pair)
  RDMA read (SCSI write), RDMA write (SCSI read)
  Send/Receive for the SCSI commands request / response, management (eg login, nops), iSCSI immediate data / unsolicited data-outs PDUs, etc

## Slide 8: iSER transport – main design issues
memory registration
  register memory in advance to avoid performance drop
  the target doesn’t advertise rdma keys hence a pool can be used for multiple clients
event management
  adopt to a design that relies on socket readability / writeability (request notification, process completion)

## Slide 9: SCSI devices
SBC - block command processing
OSD - object storage device command processing
also
  SCC - controller command processing
  MMC - multimedia command processing
  SMC - Medium Changer command processing
SCSI device API to stgt core
  lu init / config / exit
  device ops (eg TUR, INQ, SPACE, READ*, WRITE*, SEEK)
below SCSI devices a “backing store” layer further exists
  some possible types: aio, mmap, sync file

## Slide 10: STGT package (RPM)
tgtd – service
tgtd - daemon
tgtadm – admin tool
tgt-setup-lun – helper/simper admin tool (uses tgtadm)
man pages to the admin tools

## Slide 11: configuring STGT
# tgt-setup-lun -d /dev/sdy -n seed1-sdy 192.168.10.81
one liner setup which translates to the following sequence with tgtadm
create a target
# tgtadm --lld iscsi --op new --mode target --tid 1 -T iqn.2001…-seed1-sdy
add a logical unit to the target
# tgtadm --lld iscsi --op new --mode logicalunit --tid 1 --lun 1 -b /dev/sdy
bind initiators to this target instance
# tgtadm --lld iscsi --op bind --mode target --tid 1 -I 192.168.10.81

## Slide 12: configuring STGT - cont’
# tgtadm --mode target --op show
Target 1: iqn.2001-04.com.onion-seed1-sdy
System information:
Driver: iscsi
Status: running
LUN information:
LUN: 0
Type: controller (this LUN is skipped here)
LUN: 1
Type: disk
SCSI ID: deadbeaf1:1
SCSI SN: beaf11
Size: 82G
Online: Yes
Poweron/Reset: Yes
Backing store: /dev/sdy
ACL information:
192.168.10.81

## Slide 13: some performance numbers
over ramdisk (single initiator, source Voltaire)
  BW: READ – 1200 MB/sec WRITE – 870 MB/sec
  IOPS (I/O per second): READ – 62K WRITE – 66K
over ramdisk (source Pete Wyckoff et al)
  latency for some OSD ops: ping 33us, getattr – 65us
  single initiator BW : READ – 550 MB/sec WRITE – 500 MB/sec
  multiple initiators BW: both READ/WRITE reach 900 MB/sec
  few variations between READ / WRITE
    what message size gives the max BW (read 200KB, write 500KB)
    how many initiators needed to get the aggregated BW under specific message size: READ – 2 WRITE – 8

## Slide 14: STGT / community
community
  web site http://stgt.berlios.de has pointers to:
    git tree where tgt is maintained
    developers mailing list
wiki @ open-fabrics https://wiki.openfabrics.org/tiki-index.php?page=ISER-target
    explain / example usage
    download packages for RH5 U1 and SLES10 SP1

## Slide 15: references
tgt: framework for storage target drivers
Fujita Tomonori and Mike Christie. Ottawa Linux Symposium 2006
iSER Storage Target for Object-based Storage Devices
Dennis Dalessandro, Ananth Devulapalli, Pete Wyckoff
Proceedings of MSST'07, SNAPI Workshop, San Diego, CA, Sep 2007
source tree @ http://www.kernel.org/pub/scm/linux/kernel/git/tomo/tgt.git