## Slide 2: InfiniBand Routers
Ian Colloff : QLogic
LWG Co-Chair

## Slide 3: IB Routing
Why Routers
Approach
IB Routing Features
What will the specification cover
What the specification will not cover
Companies Working on the Specification
Time Line

## Slide 4: Why IB Routers
Extend the address space of an IB subnet
  GID is 128 bits vs 16 bit LID (local to a sub-net)
Provide fault containment to a single subnet
Protection beyond P_Key enforcement
  Initial goal however is to keep IB Router “dumb” for efficiency
Provide mechanisms for Long Haul links
  Many 1,000’s Km
  Router to router communication can be on links other than IB

## Slide 5: Simple Diagram
SM/SA/SRA
GRM
GRM
GRM
5 Subnets Connected by 3 Routers
GRM
GRM
Primary SM or GRM
Secondary / backup SM or GRM
Paths between Routers within a subnet, passing through one or more IB switches
SM/SA/SRA
SM/SA/SRA
SM/SA/SRA
SM/SA/SRA
SM/SA/SRA
SM/SA/SRA
IB Sub-net
IB Sub-net
IB Sub-net
IB Sub-net
IB Sub-net
Router
Router
Router
GRM Global Route Manager
SRA Subnet Route Agent

## Slide 6: Approach
Learn from our previous experience of trying to specify Routers
  Don’t fall into the same rat holes
Listen to what members (and others) want
  However the best way to influence Specification is to join the IBTA
Developing a Straw-man for IBTA Review
  Covers all the main issues
  When there is agreement work partitioned to relevant bodies
    LWG (Link Working Group) currently working on the straw-man
    MGTWG (Management Working Group) for the management activities
    SWG (Software Working Group) for path establishment (Communication Management)
NOTE: Standards bodies don’t work as fast as one would like!

## Slide 7: IB Routing Features
Enable a phased approach to enable early access
  Try to anticipate hooks for future expansion
Multiple subnets may be connected through multiple Router Hops
  Provision for other fabrics between IB Routers
  Avoid path deadlocks
  Dynamic addition and removal of sub-nets within the larger fabric
Minimize the changes to endpoint behavior in crossing multiple sub-nets
  Communication Manager (to provide a connection)
  Routers will provide backpressure

## Slide 8: IB Routing Features (continued)
Subnet Manager controls the sub-net
  Provides paths for IB-Routers to use in crossing a sub-net (deadlock free)
Support for Multicast across multiple subnets
Maintain Alternative Path Mechanism for resilience
Expand Congestion Control to cover IB Routers
Expand QoS to cover IB Routers
Ability to generate a “no single point” of failure within the wider fabric

## Slide 9: What will the specification Cover?
The interaction between the Route Manager and :-
  Route Manager: May be centralized initially
    In future this may be distributed
  Subnet Managers (SM & SA)
Generation of paths through the larger fabric
  How resources (Routers, SM, Route Managers) are identified
  Interaction with Subnet Managers and Subnet Administrators
Common and New Management Data-grams to communicate information

## Slide 10: What will the specification Cover? (continued)
How P_Keys are managed across multiple subnets
Multicast
Define forwarding through Routers
Communication across multiple subnets
  Multiple paths for reliability
Fault Containment (Alternative Path Mechanism)
Extensions for Congestion Control maintain no drop policy within the current spec
QoS across the wider Fabric

## Slide 11: What the specification will not cover
The Name server (e.g. DNS)
  How does one get a GID in the first instance
How a IB Router Port to a different fabric will function
  Provide ground rules
    Router port indicated by flag
    Packets must be in order

## Slide 12: Companies Working on the IB Router Specification
Cisco
IBM
Intel
Mellanox
Obsidian
QLogic
System Fabric Works
Voltaire
If you want to influence the specification join the IBTA

## Slide 13: Time Line
Straw-man End April ’08
First Phase Annex Anticipating Q1 ’09
Further Information
  www.infinibandta.org