## Slide 1: Reliable Multicast (RMC)
Liran Liss
Mellanox Technologies Inc.

## Slide 2: Agenda
Introduction
Model
ConnectX RMC Implementation
Semantics
API
Setup and operation
Scalability
Future work

## Slide 3: Introduction
RMC is a model that establishes multicast communication using reliable connection (RC) service in Infiniband fabrics
Guarantees reliable in-order delivery of multi-packet messages
  Currently defined for channel semantics (send-receive)
    Can be enhanced to support RDMA-W
Example applications:
  Distributed analysis of massive amounts of data
  Scaling online trading, live news and video distribution
  Speeding up of high performance MPI collective operations

## Slide 4: Model
Single sender / multiple receivers
  Multiple receivers can exist on the same host
Multiple senders achieved using multiple RMC groups
  Does not provide total-ordering
RMC group members are fixed
  Not a complex group-communication protocol
Main idea
  RC transport with an MGID destination
    Standard Send packet
  Sent packets are duplicated by switches
  Acks are aggregated by the sender
No changes in switch behavior

## Slide 5: Model – continued
RMC Responder QPz
RQ
RMC Responder QPy
RQ
RMC Responder QPx
RQ
Switch
RMC Child QPb
RMC Parent QPa
RMC Child QPc
RMC Child QPd
SQ
LID 0
LID 2
LID 3
LID 1
RQP:x DLID:1
RQP:c DLID:0
RQP:d DLID:0
RQP:y DLID:2
RQP:0xffffff DLID: MLID
RQP:z DLID:3
RQP:b DLID:0
Each RMC group requires a unique MGID
RMC Parent allows an 0xffffff RQP
RMC responder skips DestQP match

## Slide 6: ConnectX RMC Implementation
RMC Parent QP
  Owns the SQ
  Aggregates acks from children in HW
  Reports SEND completions
  Retries sends on timeout
    Normal RC behavior
Child QP
  Provides a context for receiving acks from a single responder
  Reports acks to parent
Responder QP
  Virtually connected
  Accepts MC packets and sends RC acks as usual
  Reports RECV completions

## Slide 7: Semantics
Send WQEs are completed only if all responders have acknowledged
Receive WQEs are completed as usual
  Messages are delivered independently of other responders
Any single responder that ceases to reply will eventually cause the sender QP to transition into error state
  All posted WQEs that have not completed will be flushed
  A subset of these WQEs may have been delivered to some of the responders
  This subset is not reported
  Active responders are not notified

## Slide 8: API
Userspace only (at the moment)
That’s it!
--- libibverbs.orig/include/infiniband/verbs.h
+++ libibverbs/include/infiniband/verbs.h
@@ -401,7 +401,9 @@ enum ibv_qp_type {
IBV_QPT_RC = 2,
IBV_QPT_UC,
IBV_QPT_UD,
- IBV_QPT_XRC
+ IBV_QPT_XRC,
+ IBV_QPT_RMC_PAR,
+ IBV_QPT_RMC_CHILD,
+ IBV_QPT_RMC_RESP
};
struct ibv_qp_cap {
@@ -421,6 +423,8 @@ struct ibv_qp_init_attr {
enum ibv_qp_type qp_type;
int sq_sig_all;
struct ibv_xrc_domain *xrc_domain;
+ int num_rmc_children;
+ uint32_t rmc_par_qp_num;
};

## Slide 9: RMC setup
Assume MGID ‘M’ and ‘N’ responders
Sender
  Create parent QP and modify to RTS
    QP type: IBV_QPT_RMC_PAR
    num_rmc_children: N
  Create child QPs (one per responder)
    QP type: IBV_QPT_RMC_CHILD
    rmc_par_qp_num: <parent qpn>
  Join (create) M
Responder(s)
  Create responder QP and modify to RTR
    QP type: IBV_QPT_RMC_RESP
    Initial PSN must match sender
  Attach responder QP and join M
End-to-end flow control must be disabled on all QPs

## Slide 10: RMC Operation
Initialization
  Set up parent and child QPs
  Set up responder QPs
  Prepost receive WQEs to responder QPs
    Flow control is application responsibility (E2E credits are disabled)
  Synchronize between sender and responder(s)
Sender
  Post Send WQEs to parent QP (ibv_post_send)
  Detect completions on CQ associated with parent QP
Receiver
  Post Receive WQEs to responder QPs (ibv_post_recv)
  Detect completions on associated CQs

## Slide 11: Scalability
Resource utilization
  Each MC tree uses a unique GID
  Each MC tree uses N QPs at the sender
    Can be alleviated using a MC tree hierarchy
All-to-all RMC
  N RMC trees
    Each host handles N2 QPs and N MGIDs
    Suitable for small groups only
  Hierarchal RMC trees
  Single-sender
    Dedicated node dispatches MC messages on behalf of others

## Slide 12: Future Work
Abstract setup and connection establishment
  CMA support
  Extend to All-to-all (multiple RMC setup)
Expose to kernel API
Add RDMA-W support

## Slide 13: Summary
RMC is an efficient mechanism for distributing large amounts of data to multiple hosts
  Efficient network utilization (switch replication)
  Minimal SW overheads
Supported by IB architecture with minor host-side modifications
Implemented in ConnectX HW
API patches to be submitted for review soon

## Slide 14
Thank You !