## Slide 1: Infiniband and RoCEE Virtualization with SR-IOV
www.openfabrics.org
<number>
Liran Liss, Mellanox Technologies
March 15, 2010

## Slide 2: Agenda
SR-IOV
Infiniband Virtualization models
  Virtual switch
  Shared port
  RoCEE notes
Implementing the shared-port model
VM migration
  Network view
  VM view
  Application/ULP support
SRIOV with ConnectX2
Initial testing

## Slide 3: Where Does SR-IOV Fit In?
Technique \ characteristic | Efficiency | Guest SW Transparency | Applicability | Scalability
Emulation | Low | Very high | All device classes | High
Para-virtualization | Medium | High – requires installing para-virtual drivers on the guest | Block, network | High
Acceleration | High | Medium: Transparent to apps May require device-specific accelerators | Network only, hypervisor dependent | Medium (for accelerated interfaces)
PCI device Pass-through | High | Low: Explicit device plug/unplug Device specific drivers | All devices | Low
SR-IOV fixes this

## Slide 4: Single-Root IO Virtualization
PCI specification
  SRIOV extended capability
HW controlled by privileged SW via PF
Minimum resources replicated for VFs
  Minimal config space
  MMIO for direct communication
  RID to tag DMA traffic
PF
VF
VF
Hypervisor
Guest
Guest
Guest
HW
PF driver
IB core
VF driver
IB core
VF driver
IB core
VF driver
IB core
VF
PCI subsystem

## Slide 5: Infiniband Virtualization Models
Virtual switch
  Each VF is a complete HCA
    Unique port (lid, gid table, lmc bits, etc.)
    Own QP0 + QP1
  Network sees multiple HCAs behind a (virtual) switch
  Provides transparent virtualization, but bloats LID space
Shared port
  Single port (lid, lmc) shared by all VFs
  Each VF uses unique GID
  Network sees a single HCA
  Extremely scalable at the expense of para-virtualizing shared objects (ports)
HW
QP0
QP1
1
2
3
GID
QP0
QP1
4
5
6
GID
QP0
QP1
7
8
9
GID
IB vSwitch
HW
QP0
QP1
1
GID
QP0
QP1
2
GID
QP0
QP1
3
GID
PF
VF
VF

## Slide 6: RoCEE Notes
Applies trivially by reducing IB features
  Default Pkey
  No L2 attributes (LID, LMC, etc.)
Essentially, no difference between the virtual-switch and shared-port models!

## Slide 7: Shared-Port Basics
Multiple unicast GIDs
  Generated by PF driver before port is initialized
  Discovered by SM
  Each VF sees only a unique subset assigned to it
Pkeys managed by PF
  Controls which Pkeys are visible to which VF
  Enforced during QP transitions
QP0 owned by PF
  VFs have a QP0, but it is a “black hole”
  Implies that only PF can run SM
QP1 managed by PF
  VFs have a QP1, but all MAD traffic is tunneled through the PF
  PF para-virtualizes GSI services
Shared QPN space
  Traffic multiplexed by qpn as usual
Full transparency provided to guest ib_core

## Slide 8: QP1 Para-virtualization
Transaction ID
  Ensure unique transaction ID among VFs
    Encode function ID in TransactionID MSBs on egress
    Restore original TransactionID on ingress
De-multiplex incoming MADs
  Response MADs are demux’ed according to TransactionID
  Otherwise, according to GID (see CM notes below)
Multicast
  SM maintains a single state-machine per <MGID, port>
  PF treats VFs just as ib_core treats multicast clients
    Aggregates membership information
    Communicates membership changes to the SM
  VF join/leave mads are answered directly by the PF

## Slide 9: QP1 Para-virtualization – cont.
Connection Management
  Option 1
    CM_REQ demux’ed according to encapsulated GID
    Remaining session messages demux’d according to comm_id
    Requires state (+timeout?) in PF
  Option 2
    All CM messages include GRH
      Demux according to GRH GID
    PF CM management remains stateless
  Once connection is established, traffic demux’ed by QPN
    No GRH if connected QPs reside on the same subnet
InformInfo Record
  SM maintains single state machine per port
  PF aggregates VF subscriptions
  PF broadcasts reports to all interested VFs

## Slide 10: VM Migration
Based on device hot-plug/unplug
  There is no emulator for IB HW
  There is no para-virtual interface for IB (yet)
    IB is all about direct HW access anyway!
Network perspective
  Shared-port: no actual migration
  Virtual switch: vHCA port goes down on one (virtual) switch and reappears on another
VM perspective
  Shared port: one IB device goes away, another takes its place
    Different lid, different gids
  Virtual switch: same IB device reloads
    Same lid+gids
    Future: shadow sw device to hold state during migration?

## Slide 11: ULP Migration Support
IPoIB
  netdevice unregsitered and then reregistered
  Same IP obtained by DHCP based on client identifier
    Remote hosts will learn new lid/gid using ARP
Socket applications
  TCP connections will close – application failover
  Addressing remains the same
RDMACM applications / ULPs
  Applications / ULP failover (using same addressing)
    Must handle RDMA_CM_EVENT_DEVICE_REMOVAL

## Slide 12: ConnectX2 Multi-function Support
Multiple PFs and VFs
Practically unlimited HW resources
  QPs, CQs, SRQs, Memory regions, Protection domains
  Dynamically assigned to VFs upon request
HW communication channel
  For every VF, the PF can
    Exchange control information
    DMA to/from guest address space
  Hypervisor independent
    Same code for Linux/KVM/Xen

## Slide 13: ConnectX2 Driver Architecture
PF/VF partitioning at mlx4_core
  Same driver for PF/VF, but different flows
  Core driver “personality” determined by DevID
VM flow
  Owns its UARs, PDs, EQs, and MSI-X vectors
  Hands off FW commands and resource allocation to PF
PF flow
  Allocates resources
  Executes VF commands in a secure way
  Para-virtualizes shared resources
Interface drivers (mlx4_ib/en/fc) unchanged
  Implies IB, RoCEE, vHBA (FCoIB / FCoE) and vNIC (EoIB)

## Slide 14: Xen SRIOV SW Stack
IOMMU
Hypervisor
ConnectX
mlx4_core
mlx4_core
mlx4_ib
mlx4_en
mlx4_fc
DomU
Dom0
ib_core
scsi
mid-layer
Communication
channel
Interrupts and dma from/to device
Doorbells
HW commands
tcp/ip
guest-physical to machine
address translation
mlx4_ib
mlx4_en
mlx4_fc
ib_core
scsi
mid-layer
tcp/ip
Interrupts and dma from/to device
Doorbells

## Slide 15: KVM SRIOV SW Stack
IOMMU
ConnectX
Guest Process
Kernel
Communication
channel
Interrupts and dma from/to device
Doorbells
HW commands
mlx4_core
mlx4_ib
mlx4_en
mlx4_fc
ib_core
scsi mid-layer
tcp/ip
guest-physical to machine
address translation
Interrupts and dma from/to device
Doorbells
mlx4_core
mlx4_ib
mlx4_en
mlx4_fc
ib_core
scsi mid-layer
tcp/ip
User
User
Kernel
Linux

## Slide 16: Screen Shots
# ifconfig -a
ib0 Link encap:InfiniBand HWaddr 80:00:00:4A:FE:80:00:00:00:00:00:00:00:00:00:00:00:00:00:00
BROADCAST MULTICAST MTU:2044 Metric:1
RX packets:0 errors:0 dropped:0 overruns:0 frame:0
TX packets:0 errors:0 dropped:0 overruns:0 carrier:0
collisions:0 txqueuelen:256
RX bytes:0 (0.0 b) TX bytes:0 (0.0 b)
ib1 Link encap:InfiniBand HWaddr 80:00:00:4B:FE:80:00:00:00:00:00:00:00:00:00:00:00:00:00:00
BROADCAST MULTICAST MTU:2044 Metric:1
RX packets:0 errors:0 dropped:0 overruns:0 frame:0
TX packets:0 errors:0 dropped:0 overruns:0 carrier:0
collisions:0 txqueuelen:256
RX bytes:0 (0.0 b) TX bytes:0 (0.0 b)
ib2 Link encap:InfiniBand HWaddr 80:00:00:4C:FE:80:00:00:00:00:00:00:00:00:00:00:00:00:00:00
BROADCAST MULTICAST MTU:2044 Metric:1
RX packets:0 errors:0 dropped:0 overruns:0 frame:0
TX packets:0 errors:0 dropped:0 overruns:0 carrier:0
collisions:0 txqueuelen:256
RX bytes:0 (0.0 b) TX bytes:0 (0.0 b)
ib3 Link encap:InfiniBand HWaddr 80:00:00:4D:FE:80:00:00:00:00:00:00:00:00:00:00:00:00:00:00
BROADCAST MULTICAST MTU:2044 Metric:1
RX packets:0 errors:0 dropped:0 overruns:0 frame:0
TX packets:0 errors:0 dropped:0 overruns:0 carrier:0
collisions:0 txqueuelen:256
RX bytes:0 (0.0 b) TX bytes:0 (0.0 b)
...
# lspci
03:00.0 InfiniBand: Mellanox Technologies MT26428 [ConnectX VPI PCIe 2.0 5GT/s - IB QDR / 10GigE] (rev b0)
03:00.1 InfiniBand: Mellanox Technologies Unknown device 673d (rev b0)
03:00.2 InfiniBand: Mellanox Technologies Unknown device 673d (rev b0)
03:00.3 InfiniBand: Mellanox Technologies Unknown device 673d (rev b0)
03:00.4 InfiniBand: Mellanox Technologies Unknown device 673d (rev b0)
...
# ibv_devices
device node GUID
------ ----------------
mlx4_0 00000112c9000123
mlx4_1 00000112c9010123
mlx4_2 00000112c9020123
mlx4_3 00000112c9030123
mlx4_4 00000112c9040123
...

## Slide 17: Initial Testing
Basic Verbs benchmarks, rdmacm apps, ULPs (e.g., ipoib, RDS) are functional
Performance
  VF-to-VF BW essentially the same as PF-to-PF
  Similar polling latency
  Event latency considerably larger for VF-to-VF

## Slide 18: Discussion
OFED virtualization
  Within OFED or under OFED?
Degree of transparency
  To OS? To middleware? To apps?
  Identity
    Persistent GIDs? LIDs? VM ID?
Standard management
  QoS, Pkeys, GIDs