## Slide 1: Enterprise at a Global Scale
Paul Grun
Chief Scientist
System Fabric Works
(503) 620-8757
pgrun@systemfabricworks.com

## Slide 2: Abstract
There are many classes of enterprise which are geographically dispersed and yet must behave as a single, monolithic enterprise. In one such application, a globally distributed enterprise must collect real time information which must be made available to a globally distributed network of analysts. The results of the analysis, in turn, must be presented in near-real time to field agents. Large scale ‘data shipping’ using conventional networks is not a viable option since time is of the essence in this environment.
One method for presenting such a single, worldwide face is through the use of Remote Direct Memory Access (RDMA) at 40-100 gigabits per second to interconnect a set of globally distributed enterprise data centers, in effect virtualizing the globally distributed storage and compute facilities as presented to its users. This talk discusses the use of RDMA over the wide area to virtualize a set of widely dispersed data centers.

## Slide 3: Key messages
Describe ‘storage at a distance’ as practiced in LD
Extend the concept to the enterprise

## Slide 4: Truth in Advertising
I am not a network guy….
(From Joint Techs Workshop, Salt Lake City – February 2010)

## Slide 5: Truth in Advertising
I am not a network guy….
But I am pretty interested in storage, and storage at a distance.
(From Joint Techs Workshop, Salt Lake City – February 2010)

## Slide 6
One doesn’t usually think about networks when discussing storage…
…unless there is a need for ‘storage at a distance’
Suddenly, networks become very interesting.
Consider the case of a globally distributed enterprise…
This was the key message…
Notes: <number>

## Slide 7: A globally distributed enterprise
<number>
Data
Center
Data
Center
Data
Center
Remote backup/recovery
Data collected in one place, but analyzed in another
Dissemination of information throughout the enterprise
“Scientific Productivity follows Data Locality” – Eli Dart, et al
Application mobility

## Slide 8
In time sensitive environments, data is only useful if it can be analyzed quickly, results delivered quickly, and action taken quickly
The notion of ‘Storage at a Distance’ is predicated on delivering an unprecedented level of immediacy in data access
This required a re-think of the way data is ingested, stored and accessed
<number>

## Slide 9: Logical view – global datacenter
<number>
workstations,
servers
workstations,
servers
Storage
Server
Workstations,
servers
Logical switch
Storage
Server
Storage
Server
Data
Center
Data
Center
Data
Center

## Slide 10: Data center - notional
<number>
user
Storage
Server
LAN
To remote site
To remote site
switch
…
IB switch
Users connect via a web browser
servers, workstations
IB chosen for:
Latency, b/w
Support for parallel file I/O
Reduced resource utlization (CPU/memory b/w)
Cost efficiency
Compute and storage is provided at each node
Access to all data, enterprise-wide

## Slide 11: Storage at a distance
Storage
Server
…
IB switch
Storage
Server
IB switch
OC192
ATM/SONET
IB subnet segments: 40Gb/s
WAN links: 10Gb/s
Also tested on a ‘shared wavelength’ service, with excellent results
Workstations,
Servers
WAN ‘gateway’
async/sync interface
a two port switch.

## Slide 12: Enterprise storage architecture
<number>
User app
storage client
Local Storage
Remote
Storage
Remote Storage
buffer
server
An enterprise application reads data through a storage client.
The storage client connects to each storage server via RDMA.
Thus, the user has direct access to all data stored anywhere on the system.
user
Basic idea: effectively utilize rare high bandwidth links

## Slide 13: Lustre Parallel File System – (1/2)
<number>
MDS
OSS
OSS
OSS
Persistent connection to Metadata Server (MDS) and Object Storage Servers (OSS).
user
User app
storage client
buffer
server
Local Storage
Remote Storage
All file systems mounted by storage client.
Data appears as if local;
No need for file FTP.

## Slide 14: Parallel file system – (2/2)
f/s client
server
f/s client
server
f/s client
server
mds
oss
oss
oss
Lustre, pNFS…
file, object, block level I/O
store/retrieve data using parallel disk storage
- source/sink data using multiple initiators and parallel file systems

## Slide 15: RDMA WAN
WAN Gateway is a two port switch, buffer-to-buffer transfers over the WAN
RDMA
Transport
IB Network
IB Link*
IB Phy
gateway function
IB Link*
IB Phy
WAN Link
WANPhy
gateway function
IB Link*
IB Phy
WAN Link
WANPhy
RDMA
Transport
IB Network
IB Link*
IB Phy
WAN
app buffer
app buffer
WAN gateway device
‘Losslessness’ is stretched across the WAN
Highly efficient use of available bandwidth
Scales well with multiple, concurrent data flows
RDMA/IB b/w performance: ≥ 80%
TCP/IP b/w performance : ≤ 40%
RDMA CPU usage estimated at 4x less
Notes: <number>
<number>
<number>

## Slide 16: which results in…
WAN
Compute
Compute
Compute
Storage
Storage
Storage
Logical switch
A practical, enterprise network distributed over 1000s of KMs
‘Pools’ of compute resource
‘Pools’ of storage
Notes: <number>
<number>
<number>

## Slide 17: A commercial global enterprise
<number>
Data
Center
Data
Center
Data
Center
Remote backup/recovery
Data collected in one place, but analyzed in another
Dissemination of information throughout the enterprise
Application mobility
Manhattan
New Jersey
London

## Slide 18: Distributed storage, and what else?
<number>
globally virtualized storage
Global access to enterprise data – worldwide
Flexible, agile allocation of server resources
Data protection
Reliability, resiliency
Compute
Compute
Compute
Manhattan
New Jersey
London
Storage
Storage
Storage
Logical switch

## Slide 19: Flexible, agile allocation of resources??
<number>
Compute
New Jersey
London
Storage
Storage
Storage
Logical switch
VM
VM
VM
VM
VM
VM
VM
VM
VM
VM
Put the application container where compute resource is available,
or where it is needed (temporally)
Manhattan

## Slide 20: RDMA Concept
Application
RDMA
Service
network
Application
RDMA
Service
network
Based on “channel I/O”, RDMA creates memory-to-memory pipes
RDMA delivers:
low latency
scalability
high network bandwidths
low CPU utilization
conserves precious memory bandwidth
Reduce/eliminate context switches,
Reduce/eliminate buffer copies,
Minimal CPU utilization,
Conserves server memory bandwidth.

## Slide 21
App
<number>
RDMA connects virtual buffers which may be located in different physical address spaces...
buf
NIC
App
buf
NIC
OS
OS
…even across a network.
No kernel buffer copies
No OS context switch for data transfers
Virtual-to-physical address translation in the NIC. Application accesses the NIC directly.
RDMA: initiating app targets a virtual buffer in the receiving end. Virtual addresses are carried over the network by the transport.
SEND/RECEIVE: Sender targets a destination ‘queue pair’; the destination buffer address is opaque to the sender.

## Slide 22
Extending RDMA over the WAN has been repeatedly demonstrated
NRL’s work demonstrates the value of combining structured data, RDMA over the WAN and a parallel file system
Apply the same concepts to the globally distributed enterprise
www.openfabrics.org
<number>

## Slide 23: To do list
Finish routing
  SM scalability?
Improved injection rate control
  better QoS for ‘shared wavelength’ environments
Increase LID space?
Steve Poole’s list from last night
The list from the OEM panel
…
www.openfabrics.org
<number>

## Slide 24
www.openfabrics.org
<number>
Backup

## Slide 25: System Fabric Works
System Fabric Works, Inc. delivers engineering, system integration and strategic consulting services to organizations seeking to deploy high productivity computing and storage systems, low latency high performance networks and the optimal software to meet our customer’s application requirements. SFW also offers custom integration and deployment of commodity servers and storage systems at levels of performance, scale and cost effectiveness that are not available from other suppliers. SFW personnel are widely recognized experts in the fields of high performance computing, networking and storage systems particularly in OpenFabrics Software, InfiniBand, Ethernet and energy saving, efficient computing technologies such as RDMA.
www.systemfabricworks.com

## Slide 26: An efficient WAN?
FTP packets
FTP/TCP: windowing protocol
Windowing effects are exaggerated over long distance.
Measured utilizations ~20% of wire bandwidth.
RDMA protocol keeps the pipe continuously full. Measured utilizations approach 98% of wire bandwidth.
FTP/TCP/IP
RDMA
client
client