## Slide 1: Exascale Challenges Roadmap
Lloyd Dickman, QLogic, CTO for InfiniBand Products
March 16, 2010

## Slide 2: Exascale = 103 Petascale
OFED @ 0.001 EF
  Already seeing operational performance challenges at scale
1 PF

## Slide 3: 0.001 EF: State of the Union
Largest OFED deployment ~7000 nodes
Need OFA OFED to scale subnet and connection management
MTBF of cluster < job run times
GPUs emerging

## Slide 4: 0.01 EF - 2012
OFED @ 10 PF
  Clear operational performance challenges
  Need to deal with resiliency

## Slide 5: 0.01 EF Challenges
Really need OFA OFED to scale fabric discovery and routing, also connection management
Need rapid Job Startup
Fault resilience
  Components growing O(linear)
  Interconnections growing O(>linear)
Collective communications
Connected transport model needs to evolve
  Adaptive routing
  Out of order reception

## Slide 6: 0.1 EF - 2015
OFED @ 100 PF
  RDMA model needs to evolve

## Slide 7: 0.1 EF Challenges
Messaging patterns may dramatically change with hybrid and alternate programming models
  Evolving one-sided programming models
  GPU and other ancillary processing units may require peer-to-peer communications
RDMA model may become inappropriate for PGAS large memory systems
  Memory Footprint
  Pinning
Physical integration needs to offset increasing component count
How to approach B:F ratio of 0.1 ?

## Slide 8: 1 EF Challenges
?

## Slide 9: The Golden Age of Commodity Clusters
Source: Top500.org, November 2009
MPP
Clusters
Constellations
SMP
1 TF
1 PF

## Slide 10: Is Consumer Electronics Driven Technology a Sustainable Model?
Semiconductor process: OK?
System architecture, interconnect and packaging all need to evolve