## Slide 1: RoCEE in OFED Update
www.openfabrics.org
<number>
Liran Liss, Mellanox Technologies
March 15, 2010

## Slide 2: Agenda
What is RoCEE?
  Protocol stack
  Packet format
Verbs implications
Connection management
Enabling RoCEE in OFED
Development and Availability
RoCEE in action

## Slide 3: What is RoCEE?
Infiniband transport over Ethernet
  Efficient, light-weight transport, layered directly over Ethernet L2
    FCoE equivalent for high-performance IPC traffic
  Takes advantage of DCB Ethernet
    PFC, ETS, and QCN
Rich communication services
  Reliable/unreliable connected/datagram
  Unicast and multicast
  Atomics
  APM

## Slide 4: Protocol Stack
IB
(S/D/Q)
XAUI
XFI
SGMII
IB
Ethernet
IB L3
IPv4
IB transport
RDMA
applications
L1
L2
L3
L4
TCP
SDP
Socket applications
ULP
RDS
IPoIB
Verbs

## Slide 5: Packet Format
LRH
(L2 Hdr)
IB Payload
GRH
(L3 Hdr)
VCRC
ICRC
BTH+
(L4 Hdr)
IB Payload
GRH
ICRC
BTH+
FCS
MAC
ET
RoCEE
Infiniband
RoCEE

## Slide 6: Verbs Implications
Address Vectors
  IB compliant syntax
  GID-based addressing
    LID field is reserved
GIDs
  Populated with link-local address corresponding to port MAC
Special QPs
  QP0 is reserved
  QP1 is used for connection management
    Possibly other mad services in the future

## Slide 7: Connection Management
SA is out
Based on RDMACM
  OS IP stack used to resolve remote IP to DMAC and bind to outgoing Ethernet interface
    VLAN determined according to bound netdev
    RoCEE device selected accordingly
  Network parameters (MTU, SL, timeout) obtained locally according to kernel policy
  Connection proceeds with CM as in IB
Working only with Verbs also possible

## Slide 8: Enabling RoCEE in OFED
mlx4_ib
uRDMACM
RDMACM
CM
Ib_core
libmlx4
uVerbs
Ethernet Hardware
RDMA ULPs
Application
mlx4_core
mlx4_en
TCP/IP
Synch state with Eth device
Additional RoCEE port transport
RoCEE device binding + address resolution
TCP/IP stack
OFED stack
Address resolution

## Slide 9: Development and Availability
Kernel patches
  v0: Initial version, RoCEE flows in SA handled locally
  v3: Separate RoCEE SA emulation code from IB
  v4: Removed all SA emulation code altogether; CMA enhanced to support RoCEE flows
  v5: code simplifications; remove user-space MAD interface
  v7: loopback support; introduce ‘link-layer’ port attribute
  v8: add VLAN support; rebase to 2.6.33-rc3
OFED
  Initially in separate branch
  Now part of OFED-1.5.1
    GA quality!
    Well tested!

## Slide 10: RoCEE in Action (1)
sw419:~/OFED-1.5.1-20100316-0817 # ibv_devinfo hca_id: mlx4_0 transport: InfiniBand (0) fw_ver: 2.7.806 node_guid: 0002:c903:0008:e798 sys_image_guid: 0002:c903:0008:e79b vendor_id: 0x02c9 vendor_part_id: 26428 hw_ver: 0xB0 board_id: MT_0DD0120009 phys_port_cnt: 2 port: 1 state: PORT_INIT (2) max_mtu: 2048 (4) active_mtu: 2048 (4) sm_lid: 0 port_lid: 0 port_lmc: 0x00 link_layer: IB
port: 2 state: PORT_ACTIVE (4) max_mtu: 2048 (4) active_mtu: 1024 (3) sm_lid: 0 port_lid: 0 port_lmc: 0x00 link_layer: Ethernet

## Slide 11: RoCEE in Action (2)
sw419:~ # ifconfig eth2 20.4.3.219
sw419:~ # vconfig add eth2 7
Added VLAN with VID == 7 to IF -:eth2:- sw419:~ # ifconfig eth2.7 20.4.3.219
sw419:~ # cat /sys/class/infiniband/mlx4_0/ports/2/gids/0 fe80:0000:0000:0000:0202:c9ff:fe08:e799 sw419:~ # cat /sys/class/infiniband/mlx4_0/ports/2/gids/1 fe80:0000:0000:0000:0202:c900:0708:e799
sw419:~ # ibv_rc_pingpong -g 0 -i 2 sw420 local address: LID 0x0000, QPN 0x00004f, PSN 0xef4670, GID fe80::202:c9ff:fe08:e799 remote address: LID 0x0000, QPN 0x00004f, PSN 0xd454d5, GID fe80::202:c9ff:fe08:e811 8192000 bytes in 0.01 seconds = 4807.51 Mbit/sec 1000 iters in 0.01 seconds = 13.63 usec/iter
sw419:~ # ibv_rc_pingpong -g 1 -i 2 sw420 local address: LID 0x0000, QPN 0x04004f, PSN 0xe10208, GID fe80::202:c900:708:e799 remote address: LID 0x0000, QPN 0x04004f, PSN 0x9b281b, GID fe80::202:c900:708:e811 8192000 bytes in 0.01 seconds = 4857.40 Mbit/sec 1000 iters in 0.01 seconds = 13.49 usec/iter

## Slide 12: RoCEE in Action (3)
sw419:~ # ifconfig eth2 20.4.3.219
[root@mtlsqt124 ~]# rds-stress -s 11.4.5.125 -q 4096 -t 2 -d 2 connecting to 11.4.5.125:4000 negotiated options, tasks will start in 2 seconds Starting up.... tsks tx/s rx/s tx+rx K/s mbi K/s mbo K/s tx us/c rtt us cpu % 2 40137 40126 322928.84 0.00 0.00 10.91 156.89 -0.99 2 39971 39987 324128.14 0.00 0.00 10.03 157.00 -1.00 2 37488 37575 304354.64 0.00 0.00 10.59 168.45 -1.00 2 38581 38604 312945.17 0.00 0.00 10.88 161.39 -1.00 2 38429 38473 311815.57 0.00 0.00 10.54 163.22 -1.00 2 39010 38856 315703.93 0.00 0.00 10.50 163.27 -1.00 2 37104 37167 300838.65 0.00 0.00 10.27 170.97 -1.00 2 39761 39826 322698.14 0.00 0.00 10.78 159.99 -1.00 2 38787 38704 314205.64 0.00 0.00 10.69 161.82 -1.00 2 40924 41002 332171.96 0.00 0.00 11.09 153.17 -1.00 2 38844 39012 315659.80 0.00 0.00 10.53 162.44 -1.00

## Slide 13: RoCEE in Action (4)
RoCEE really rocks!!!