## Slide 1: Open Fabrics Workshop 2010
Bob Woodruff
Issues for Exascale, Scalability, and Resilience

## Slide 2: Exascale Vision
From Sunday night…. The Vision….
  1 Billion cores
  10-100s of Million nodes and MPI ranks
  Terabits of Bandwidth
  100s to 1000’s of PFs!!!!!
I can do that!!! I can do that !!! I can do that!!!
Going Further than ever before…

## Slide 3: The Reality
Monday morning…. Back to Reality….
How am I going to do that??????

## Slide 4: Scalability enhancements What we can do now
InfiniBand node count limitations
Increase LID space in the InfiniBand protocol ?
Finish the router specification and build full speed routers ?
Or go back to Ethernet that does not have these limitations?
Connection Management
Reliable connections (RC) do not scale
  Memory footprint too big, SA queries do not scale
  Can we use a dynamic connection scheme ?
    Establish and tear down connections for each I/O?
      QP transitions would have to be really fast!!!
      Memory registration needs to be really fast!!!
Do we use unreliable datagram's instead ?
  Requires S/W retries for lost packets
  Requires data copies

## Slide 5: Scalability enhancements
Datagram's with DDP?
Does not have the connection scaling issues.
Use something like tag-matching ?
  Issues with linear search when matching tags may be an issue
Can we invent something like tag-matching without the scaling limitations.
  Perhaps relax some of the MPI message ordering restrictions ? (for MPI 3?)
Memory registration costs
Can we make memory registration a speed path operation ?
Memory registration costs are too high
  not as big of a problem with disk storage (since seek times are high)
Maybe more of an issue for storage when low latency SSDs hit the market.

## Slide 6: Resiliency
Being able to tolerate H/W failures
Multipath and redundancy a must in the fabric
Being able to tolerate node failures
Fast detection of hardware failures
  End to end data protection and failure detection
Better S/W handling of failures
  More than just checkpoint/restart
  At Exascale, MTBF is so low that checkpoint/restart in MPI will not be adequate