## Slide 1: Virtual NICs and HBAs
Implementation update and usage
www.openfabrics.org
<number>
Liran Liss, Mellanox Technologies
March 17th, 2010

## Slide 2: Agenda
Stateless bridging
FCoXX
  Operation
  Driver stack
  User perspective
  Futures
EoIB
  Operation
  Driver stack
  User perspective
  Futures

## Slide 3: Stateless Bridging
Bridge does not hold any state beyond a single packet
Servers “speak” the target protocol
Converged network is only a conduit between the host and the bridge
  Native protocol PDUs are carried (encapsulated) over the converged fabric protocol
External network (Eth/FC)
Internal converged network
(Eth/IB)

## Slide 4: Fibre Channel over Ethernet/IB
Each external port is associated with a Virtual NPIV (vNPIV) set
  Represents FC connectivity within the internal network
  Appears as a normal NPIV port to SAN
  Holds a context table containing a record for each vHBA
GW logs in to SAN and translates host FLOGI packets to FDISC
FC SAN

## Slide 5: FCoXX – Data Path Operation
Host
  Egress – destination address is always the gateway
  Ingress – FC Frame extracted from payload and processed by vHBA
Gateway
  From FC network
    Looks up D_ID and send encapsulated frame to host
    If lookup fails, packet is dropped
  From vHBA
    Data frames: sent out on the FC port after source validation
    Control frames: gateway executes the login

## Slide 6: FCoXX Driver
Driver modules
  drivers/scsi/mlx4_fc/ml4x_fc.ko
  drivers/scsi/mlx4_fc/ml4x_fcoib.ko
Interfaces
  ib_core for InfiniBand services (FCoIB)
  Net device subsystem for FIP (FCoE)
  mlx4_core for data path HW offloads
Control plane
  Discovery & logon
    FIP for FCoE
    FIP-based for FCoIB
Data plane
  Registers normal SCSI device to SCSI midlayer
  Processes SCSI commands
    FC exchanges completely offloaded in HW

## Slide 7: Software Stack
IB HCA
ConnectX
Hardware
Specific Driver
MLX4 core
MAD
InfiniBand Verbs / API
SA
SCSI Disk
libhbaapi
openfcoe provider
Hardware
Provider
Mid-Layer
Upper Layer Protocol
User APIs
Kernel Space
User Space
Application Level
SMA
FS
access
Block
Storage
Access
MLX4 EN
MLX4 IB
mlx4_fc
mlx4_fciob
scsi mid-layer
libfcoe
libfc
fc_scsi_transport
Management
File System
Net device
queuecommand()
done()

## Slide 8: Discovery
<number>
FCoE (open-fcoe.org model) | FCoIB
ETH stack affects FCoE stack Ifconfig up/down, mtu change, … | FC stack depends on IB, but IB user actions don’t influence FC operation
Manual vHBA creation echo eth3.200 > /sys/…/create | Automatic vHBA creation
Single vHBA per {port,vlan} | Many vHBAs per {port,pkey}
FIP embedded in vHBA | FIP controls creation/destruction of vHBAs
FIP selects a single GW (highest prio) on each port | FIP can create multiple vHBAs (e.g., one per GW) Based on policy or management
VLANs discovery implemented in user-space Daemon should create the vlan interface and then vHBA | PKey discovery from kernel-space In the same FIP module

## Slide 9: Usage
Load the driver
  modprobe mlx4_fc
Use the disk!
  mount /dev/sda2 /mydir

## Slide 10: Futures
Same look and feel as normal FC HBAs
OS support:
  Linux: FCoE and FCoIB in Beta quality
    GA + kernel submission in a couple of months
  VMware:
    FCoIB in alpha
    FCoE in work
  Windows:
    Under work

## Slide 11: Ethernet over IB (EoIB)
Each external port is associated with one or more Virtual Hubs (vHubs)
vHub
  Represents an Ethernet broadcast domain within the internal network (VLAN)
  Holds a context table containing a record for each vNIC
    The context table is distributed to all vNICs
  Associated with 3 IB multicast groups
    Broadcast
    Context table updates
    Context table distribution
IB_path, myQP, dQP
IB_path, myQP, dQP
MAC/VLAN
MAC/VLAN
:
:
GW port
GW port
Eth
Eth
Eth
Eth
Eth
Eth
Eth
Eth
Ethernet wires
vHUB2
MAC
payload
Pkey
VLAN
MAC
payload
Pkey
VLAN
MAC
payload
Pkey
Eth. frame
IB encapsulation hdr
Default
Gateway
IB_path, myQP, dQP
IB_path, myQP, dQP
MAC/VLAN
MAC/VLAN
Default
Drop or Promiscuous
:
:
InfiniBand Fabric

## Slide 12: EoIB Data-path Operation
Host
  TX: driver looks up the destination address {DMAC, VLAN} on the vHub context table
    On hit: forward to host using matching IB address
    On miss: forward to gateway
  RX: deliver encapsulated Ethernet frames to netdevice
Gateway
  Egress packets are de-capsulated and delivered to the corresponding Ethernet port
  Ingress packets are associated to a vHub based on VLAN ID, and then sent to the corresponding host

## Slide 13: EoIB Driver
Single object: drivers/net/mlx4_vnic/ib_ml4_vnic.ko
Interfaces
  Ib_core for InfiniBand services (e.g., multicast)
  mlx4_core for data path HW offloads
Control plane
  Discovery & logon based on FIP
  Context maintenance
Data plane
  Registers normal Ethernet netdevice
  Implements standard offloads
    Tx/Rx TCP/UDP checksums
    TSO/LRO
    TSS/RSS
    Interrupt moderation

## Slide 14: Software Stack
IB HCA
ConnectX
Hardware
Specific Driver
MLX4 core
MTHCA
MAD
InfiniBand Verbs / API
SA
User Level Verbs / API
SDP
IPoIB
SRP
iSER
UDAPL
SDP Library
User Level MAD API
Open SM
Diag
Tools
Hardware
Provider
Mid-Layer
Upper Layer Protocol
User APIs
Kernel Space
User Space
Application Level
SMA
Sockets
Based Access
Various
MPIs
Block
Storage
Access
IP Based
App
Access
MLX4 EN
MLX4 IB
vNIC
netdev
vNIC
discovery
MLX4
vNIC

## Slide 15: Gateway Discovery
Advertise Initiated Discovery
Solicitation Initiated Discovery

## Slide 16: Login and Context Management

## Slide 17: EoIB Data Plane
core0
core1
core2
core3
RX RING
port0
port1
vnic0 (netdev0)
EQ
SRQ
RX RING
EQ
SRQ
RX RING
EQ
SRQ
RX RING
EQ
SRQ
RX RING
EQ
SRQ
RX RING
EQ
SRQ
RX RING
EQ
SRQ
RX RING
EQ
SRQ
RX
CQ
RX
CQ
RX
CQ
RX
CQ
LRO NAPI
LRO NAPI
LRO NAPI
LRO NAPI
vnic1 (netdev1)
RX
CQ
RX
CQ
RX
CQ
RX
CQ
LRO NAPI
LRO NAPI
LRO NAPI
LRO NAPI
TX RING
TX CQ
TX RING
TX CQ
TX RING
TX CQ
TX RING
TX CQ
TX RING
TX CQ
TX RING
TX CQ
TX RING
TX CQ
TX RING
TX CQ
2 IB ports
4 cores
2 vnics on IB port0
RSS_size = 4
#TX rings = #cores per vnic - #RX rings= #cores per port
QP1
QP2
QP3
QP4
QP1
QP2
QP3
QP4

## Slide 18: vNIC Types
Network Administered Mode
  vNICs are created / destroyed / enabled / disabled by the network administer
  When a host is disconnected its vNICs disappear
Host Administered Mode
  vNICs managed by host administrator
  When host is disconnected its vNICs bring down the link

## Slide 19: Host Administered Usage
vNICs managed via standard configuration files
  E.g., /etc/sysconfig/network-script/ifcfg-eth2
System service reads the configuration file and creates / destroys corresponding vNICs
  Service is a standard init.d script in Linux
    /etc/init.d/network-vnic {start | stop | restart | reload | status}
  Service runs on boot
    Ensures consistency between host reboots
  Host admin can modify the configuration file and restart service at anytime

## Slide 20: Configuration File Example
cat /etc/sysconfig/network-scripts/ifcfg-eth2
# Mellanox Technologies Virtual NIC #1
DEVICE=eth2
BOOTPROTO=none
HWADDR=00:30:48:7d:de:e4
ONBOOT=yes
IPADDR=11.20.1.22
NETMASK=255.255.0.0
TYPE=Ethernet
BXADDR=00:00:02:c9:03:11:03:0f
BXEPORT=A10
VNICVLAN=0
VNICIBPORT=mlx4_0:1
cat /etc/sysconfig/network-scripts/ifcfg-eth3
# Mellanox Technologies Virtual NIC #2
DEVICE=eth3
BOOTPROTO=none
HWADDR=00:30:48:7d:de:e5
ONBOOT=yes
IPADDR=11.20.1.23
NETMASK=255.255.0.0
TYPE=Ethernet
BXADDR=00:00:02:c9:03:11:03:0f
BXEPORT=A11
VNICVLAN=7
VNICIBPORT=mlx4_0:1
Standard network settings as supported by the Operating System services
vNIC configuration supported by network-vnic service
If no MAC is provided, the service will generate one; auto-generated macs are cached for consistency

## Slide 21: Configuration Service Example
/etc/init.d/network-vnic start
Creating Virtual NIC interface eth2: [ OK ]
Creating Virtual NIC interface eth3: [ OK ]
Creating Virtual NIC interface eth4: [ OK ]
/etc/init.d/network start
Bringing up interface eth0: [ OK ]
Bringing up interface eth1: [ OK ]
Bringing up interface eth2: [ OK ]
Bringing up interface eth3: [ OK ]
Bringing up interface eth4: [ OK ]
Bringing up interface eth5: [ OK ]
Bringing up interface eth6: [ OK ]
Bringing up interface eth7: [ OK ]
/etc/init.d/network-vnic status
Name Admin-Mode IB-Port BX-Address BX-Eport MAC-Address VLAN
---- ---------- -------- ----------------------- -------- ------------------------ --------
eth2 Host mlx4_0:1 00:00:02:c9:03:11:03:0f A10 00:30:48:7d:de:e4 0 (disabled)
eth3 Host mlx4_0:1 00:00:02:c9:03:11:03:0f A11 00:30:48:7d:de:e5 7
eth4 Host mlx4_0:2 BX002_QA_LAB A12 00:25:8b:01:00:01 (auto) 7
eth5 Network mlx4_0:1 BX001_QA_LAB A10 00:25:8b:00:0c:02 (auto) 0 (disabled)
eth6 Network mlx4_1:1 BX001_QA_LAB A11 00:25:8b:00:0c:03 (auto) 0 (disabled)
eth7 Network mlx4_1:2 BX001_QA_LAB B11 00:25:8b:00:0c:04 (auto) 13
eth0/eth1 are standard physical NICs
eth2/eth3/eth4 are Mellanox Host Admin Virtual NICs
eth5/eth6/eth7 are Mellanox Network Admin Virtual NICs

## Slide 22: EoIB Futures
Internal vHub
Link aggregation
OS support
  Linux: available today
    Kernel submission in a few months
      OFED integration will follow
  VMware: alpha
  Windows: under work
  Solaris: under work