## Slide 1: Hybrid and Manycore Architectures
Jeff Broughton
Systems Department Head, NERSC
Lawrence Berkeley National Laboratory
jbroughton@lbl.gov
March 16, 2010
www.openfabrics.org
<number>

## Slide 2: Exascale in Perspective
1,000,000,000,000,000,000
flops/sec
1000 × U.S. national debt in pennies
100 × number of atoms in a human cell
1 × number of insects living on Earth

## Slide 3: Exascale in Perspective
1
flop/sec
1938 – Zeus Z1

## Slide 4: Exascale in Perspective
1,000
flops/sec
1938 – Zeus Z1
1946 – ENIAC

## Slide 5: Exascale in Perspective
1,000,000
flops/sec
1938 – Zeus Z1
1946 – ENIAC
1961 – IBM 7030 “Stretch”

## Slide 6: Exascale in Perspective
1,000,000,000
flops/sec
1938 – Zeus Z1
1946 – ENIAC
1961 – IBM 7030 “Stretch”
1983 – Cray X-MP
Vector

## Slide 7: Exascale in Perspective
1,000,000,000,000
flops/sec
1938 – Zeus Z1
1946 – ENIAC
1961 – IBM 7030 “Stretch”
1983 – Cray X-MP
1997 – ASCI Red
Cluster/MPP
Vector

## Slide 8: Exascale in Perspective
1,000,000,000,000,000
flops/sec
1938 – Zeus Z1
1946 – ENIAC
1961 – IBM 7030 “Stretch”
1983 – Cray X-MP
1997 – ASCI Red
2008 – Roadrunner
Cluster/MPP
Vector

## Slide 9: Exascale in Perspective
1,000,000,000,000,000,000
flops/sec
1938 – Zeus Z1
1946 – ENIAC
1961 – IBM 7030 “Stretch”
1983 – Cray X-MP
1997 – ASCI Red
2008 – Roadrunner
2018? – Exascale
Hybrid/Manycore
Cluster/MPP
Vector

## Slide 10: Why Multicore/Manycore?
Processor clock speeds have hit a wall
  15 years of exponential improvement has ended
Cores per chip growing per Moore’s Law
  Doubling every 18 mos.
But, power is the new limiting factor
<number>
Notes: Check order of trends in overview
User demand for exascale
<number>

## Slide 11: Energy Cost Challenge for Computing Facilities
goal
usual scaling
2005 2010 2015 2020
<number>
1 petaflop in 2010 will use 3 MW
1 exaflop in 2018 possible with 200 MW with “usual” scaling
1 exaflop in 2018 at 20 MW is DOE target

## Slide 12: Memory Technology – Bandwidth costs power

## Slide 13: Off-chip Data Movement Costs More than FLOPs
www.openfabrics.org
<number>
Intranode
MPI
On-chip
CMP
Intranode
SMP
Flop

## Slide 14: Implications
No clock increases  hundreds of simple “cores” per chip
Less memory and bandwidth  cores are not MPI engines
Current multicore systems too energy intensive  more technology diversity (GPUs, SoC, etc.)
Programmer controlled memory hierarchies likely
www.openfabrics.org
<number>
  Applications, Algorithms, System Software will all break

## Slide 15: Exascale “Swim Lanes”
Complex Multicore | Maintain complex cores, and replicate | X86 Power7
GPU / Accelerators | Use highly specialized processors adapted from gaming | Nvidia Fermi Cell
SoC / Embedded | Use many simpler, lower power cores from embedded space | BlueGene GreenFlash

## Slide 16: Collision or Convergence?
CPU
GPU
multi-threading
multi-core
many-core
fixed function
partially programmable
fully programmable
?
programmability
parallelism
after Justin Rattner, Intel, ISC 2008
Notes: <number>

## Slide 17: SoC/Embedded Swim Lane
<number>
Cubic power improvement with lower clock rate due to V2F
Slower clock rates enable use of simpler cores
Simpler cores use less area (lower leakage) and reduce cost
Tailor design to application to REDUCE WASTE
Intel Core2
Intel Atom
Tensilica XTensa
Power 5
This is how iPhones and MP3 players are designed to maximize battery life and minimize cost

## Slide 18: SoC/Embedded Swim Lane
<number>
Intel Core2
Intel Atom
Tensilica XTensa
Power 5
Power5 (server)
  120W@1900MHz
  Baseline
Intel Core2 sc (laptop) :
  15W@1000MHz
  4x more FLOPs/watt than baseline
Intel Atom (handhelds)
  0.625W@800MHz
  80x more
Tensilica XTensa DP (Moto Razor) :
  0.09W@600MHz
  400x more (80x-100x sustained)

## Slide 19: Hybrid Cluster Architecture with GPUs
www.openfabrics.org
<number>
CPUs
Memory
GPU
InfiniBand/
Ethernet
PCI Buses
Northbridge

## Slide 20: Some alternative solutions providing unified memory
www.openfabrics.org
<number>
Memory
InfiniBand/
Ethernet
CPU
Memory
GPU
InfiniBand/
Ethernet
GPU
CPU
QPI/HT

## Slide 21: Where does OpenFabrics/RDMA fit?
Core-to-Core? No.
The machine is not flat.
  Can’t pretend every core is a peer.
  Strong scaling on chip; weak scaling between chips.
Lightweight messaging required.
  Many smaller messages
  One-sided ops / Global addressing
  Connectionless?
  Ordering?
Size and complexity of an HCA is >> a single core
  ~20-40X die area
  ~30-50X power
www.openfabrics.org
<number>

## Slide 22: Where does OpenFabrics/RDMA fit?
Node-to-Node? Maybe.
  GPUs: MPI likely present at this level between hosts
  SoC: Extending core-to-core network may make sense
  Either: I/O must be supported.
Target BW: 200-400GB/s per node
  What data rate will we have in 2018?
  Silicon Photonics?
SoC design argues for NIC on die
  Dedicate many simple cores to processing packets?
  Can share the TLB -> smaller footprint
www.openfabrics.org
<number>

## Slide 23: Exascale will transform computing at every scale
Significant advantages even at smaller scale
Cannot afford Exascale to be a niche
Requires technology & software continuity across scales to get sufficient market volume

## Slide 24: Looking into the Future
www.openfabrics.org
<number>
1 Zettaflop
in 2030

## Slide 25: Thank You!
www.openfabrics.org
<number>