## Slide 1: New Direction Proposal: An OpenFabrics Framework for high-performance I/O apps
OFA TAC, Key drivers: Sean Hefty, Paul Grun

## Slide 2: OFA Board Ask
Create an OpenFramework (OFWG) working group to:
  Develop, test, and distribute:
    An extensible, open source framework that provides access to high-performance fabric interfaces and services.
    Extensible, open source interfaces aligned with ULP and application needs for high-performance fabric services.
  OFWG will not create specifications, but will work with standards bodies to create interoperability as needed

## Slide 3: Application-centric I/O
“Application-centric I/O” is the art and science of defining an I/O architecture that maximizes application effectiveness
What distinguishes OFA as an I/O provider is that it has always relied on this “tops down” principle
RDMA is based on the principle of Application-centric I/O
app
app
i/f
Fabric provider
i/f
Fabric provider
Critically important!
Notes: Application-centric I/O – a hallmark of OFA as an I/O provider.
Designing according to the principles of application-centric I/O means beginning with a clear understanding of an application’s I/O requirements. In the case of RDMA, the application requirement being met was for low latency message passing.

## Slide 4: What we mean by “RDMA”
“RDMA” means Remote Direct Memory Access.
It means that two applications can communicate directly over a network.
Its design was driven by application requirements for low latency.
RDMA is a classic example of application-centric I/O: It was specifically developed to support scale-out of message-passing applications
Notes: RDMA was designed by applying the principles of Application-centric I/O.
Meeting the application requirements for low latency meant creating a pipe, or I/O channel directly into application user space. This required implementation of the channel I/O hardware, and providing a s/w interface to the channel.

## Slide 5: RDMA architecture
Session
Transport
RDMA protocols
Transport
App interface
Application
Network
Link
Phy
Verbs Definition
RDMA Protocols
N/W Transport
Roughly speaking…
Interface definition
I/O Service
RDMA architecture includes an I/O Channel and an interface to the I/O Channel
Notes: RDMA architecture includes an I/O service and an interface definition.
Next, we show how this is implemented in OFS.

## Slide 6: How RDMA is deployed in OFS
app
RDMA
Service
other
services
Verbs API
Fabric Provider Layer
Interface Layer (supplied by OFA today)
Application Layer
* The fabric provider could be IB, or iWARP, or RoCE. All are providers of RDMA services.
technology specific fabric*
Primary focus: low latency for cluster applications
Notes: A Practical Implementation of Application-centric I/O
Includes an interface specification (verbs) and implementation (verbs API) and standards-based providers of I/O services.
The interface layer (i.e. the Verbs API) provides application access to an RDMA I/O Service. The RDMA service is provided by various vendors.

## Slide 7: Historical RDMA design flow
App reqmts (e.g. low latency) drove fabric characteristics
IBTA specified an RDMA service:
  send/receive,
  RDMA RD. RDMA WRT…
OFA implemented the API
app
RDMA
Service
Verbs API
1
2
3
In the case of OFA, the RDMA Service was designed first (including the Verbs specification), followed by the Verbs API. This is still an application-centric approach to I/O.
other
services
technology specific fabric*
Notes: Designing an Application-centric I/O service.
Even though the RDMA service was defined first, this is STILL an application-centric I/O, it just happens that the interface (the verbs API) was defined *after* the fabric had been specified. So yes, it is a “bottoms up approach” to designing an application-centric I/O architecture.

## Slide 8: OFS today
Hardware Layer
Application layer
Upper layer protocols
RDMA Provider Layer
Application interface layer – OFS s/w
RDMA Fabric Provider layer – IB, iWARP, RoCE…
Verbs API
There has been some splintering of the I/O interface
Notes: Problem space: A splintering of the I/O interface?
OFA began by implementing a single, clean interface: the Verbs API based on the Verbs specification. Over time, a series of ULPs have been added to smooth and accelerate the adoption of RDMA. Thus, today we have several ‘interfaces’ to the RDMA service to meet different needs. For lowest latency, code to the verbs. For block storage access, use the SRP or iSER ULPs. Eventually PSM emerged as a higher performance interface mainly for MPI applications. We are seeing a slight splintering of the interface layer.

## Slide 9: This works fine, except…
The world is demanding new ways of analyzing avalanches of data
   Big Data
People want to store and access data in new ways
   the Cloud
Larger, complex problems are requiring new collaboration methods
   Data access over long distances
In short, “application requirements” continue to shift over time
Notes: Problem Space – New usages driving new application requirements. And we want to broaden the OFA’s appeal.
There are significant changes in the way computer systems are used. This may change the way applications access and use I/O services, leading to further splintering of the clean verbs interface. For example, Big Data usages require access to unstructured data. Or Cloud Computing requires a pool of storage accessible over the web. Or scientists collaborating over extremely large data sets require methods to share access to a single storage repository. E.g. Sq Km Array

## Slide 10: Not only that, but…
There are now requirements to scale applications to run on increasingly large HPC clusters
There are requirements to run applications on new compute models e.g. heterogeneous computing (x86 + GPU)
There are new requirements to run Apps on many-, multi-core processors
Requirement to take advantage of shared memory architectures
…
What should we be doing to ensure the I/O model remains “application-centric”?
Notes: Problem Space – evolving technology is driving new application I/O usages.
Even in classical HPC, the environment is evolving in ways that may require different I/O services or different ways to access those I/O services.

## Slide 11: So what to do?
Hardware Layer
Application Interface
Application layer
Provider Layer
Examine the classes of applications that are important to target users of OFS.
Let the applications drive the appropriate interface definition.
This, in turn, drives the necessary features that the fabric should support.
Different classes of applications may require different types of I/O services
Notes: Solution Space – apply the principles of Application-centric I/O rigorously.
An Example: an MPI application may require the provider layer to provide a collectives service.

## Slide 12: Classes of applications
Device
Hardware
Specific Driver
Connection Manager
MAD
Kernel verbs
SA Client
Connection
Manager
Connection Manager
Abstraction (CMA)
Open SM
Diag
Tools
Hardware
Provider
Mid-Layer
User verbs
User APIs
SDP
IPoIB
SRP
iSER
RDS
Upper Layer Protocol
NFS-RDMA
RPC
Cluster
File Sys
Application Level
SMA
Clustered
DB Access
Sockets
Based Access
Various
MPIs
Access to
File
Systems
Block
Storage
Access
IP Based
App
Access
Applications supported by OFS today
Notes: Solution Space – this approach is not limited to just low latency I/O, or clusters.
We are about to introduce the notion of Classes of Applications. These are nothing more than convenient buckets.

## Slide 13: Mapping apps to classes
Legacy apps (skts, IP)
Data Analysis
Data Storage, Data Access
Distributed Computing
Filesystems
Object storage
Block storage
Distributed storage
Storage at a distance
Via msg passing
MPI applications
Structured data
Unstructured data
Skts apps
IP apps
Via shared memory
- PGAS languages
Application Level
Clustered
DB Access
Sockets
Based Access
Various
MPIs
Access to
File
Systems
Block
Storage
Access
IP Based
App
Access
Are these the right classes of applications of interest to targeted OFS users?
Notes: Mapping the supported applications to classes.
The most significant additions are:
Unstructured Data aka support for Big Data (so far, nobody has any idea what we need in the I/O architecture for Big Data…yet)
Storage at a Distance
Distributed Computing via shared memory (PGAS, SHMEM…)

## Slide 14: Tops down architecture
app
Service…
interface
1. As before, app reqmts drive the flow
3. Which drives the on-the-wire protocols
2. Which drives the app interface
Service…
Service…
Verbs is the interface to an RDMA service.
The implications are:
To better support more classes of applications we may need to provide more types of I/O service
Which means that there may be more than one type of interface
technology specific fabric*
Notes: A risk of further splintering – we may require multiple services and multiple interfaces

## Slide 15: A framework
Fabric Interfaces
I/F
I/F
I/F
I/F
Fabric Provider Implementation
I/O service
I/O service
I/O service
Framework defines multiple interfaces
Vendors provide optimized implementations
The framework exports a number of I/O services (e.g. an RDMA service, a collectives offload service, an Atomics service, etc) via a series of defined interfaces.
Notes: Solution Space – provide a framework allowing applications to select the appropriate I/O service(s), and allowing vendors to select which I/O services to implement.

## Slide 16: A word about interoperability
application
wire packets
I/O stack
For interoperability, industry standards may be required here and/or here
OFA will not specify standards, but will work with appropriate standards bodies as needed.
Notes: A word of caution – this is probably larger than just the OFA. It will require cooperating with industry standards bodies such as the IBTA, or IEEE, or IETF or…

## Slide 17: Sticking w/ 1st principles
Remember this?
“Application-centric I/O” is the art and science of defining an I/O subsystem that maximizes application effectiveness.
The objective of the framework approach is to provide I/O services that are responsive to application needs, but do not limit us to a single interface or I/O paradigm
Notes: Application-centric I/O begins by understanding the I/O characteristics of a given application, or class of applications.
Scalability requirements
Performance requirements
Reliability characteristics
Understanding these issues leads to a definition of the character of the I/O infrastructure, e.g.
Connection oriented, Connectionless
Unicast, Multicast
Atomics
Direct memory access
  Channel oriented access
  Memory oriented access
Protection and isolation mechanisms
Latency vs b/w optimization
Large vs small message operations
Characteristic topologies
Management paradigms (centralized vs autonomous configuration)
Deadlock avoidance
and so on.

## Slide 18: Proposal
  Form a working group to develop an OpenFabrics framework
  The open fabrics framework allows:
  apps to select appropriate I/O services and the interface to those services
  Vendors to selectively provide I/O services
  The OpenFabrics framework exports low-level fabric services
    Focus on abstracted hardware functionality
  RDMA (and the verbs i/f to it) is a core I/O service
    Other I/O services to be defined and incorporated
  Design extension support into the fabric framework

## Slide 19: Proposed OpenFabrics Framework
Fabric Framework
OFA Provider(s)
IB Verbs
Verbs Provider
Verbs
Fabric Interfaces
Transition from providing verbs API
to providing fabric interfaces
…

## Slide 20: Framework example
Fabric Interfaces (examples only)
Address Resolution
Provider
Info
RDMA
Atomics
Active Messaging
Tag Matching
Collective Operations
CM Services
Fabric Provider Implementation
Address Resolution
CM Services
RDMA
Atomics
Collective Operations
Framework defines multiple interfaces
Vendors provide optimized implementations

## Slide 21: Next Steps
Get moving on developing this Framework!
Recommend starting a WG to focus development efforts

## Slide 22: Voteable
The OFA Board votes to create an OpenFramework Working Group (OFWG) within the OFA’s bylaws with the following charter:
  Develop, test, and distribute
    An extensible, open source framework that provides access to high-performance fabric interfaces and services.
    Extensible, open source interfaces aligned with ULP and application needs for high-performance fabric services
  Work with standards bodies as needed to create interoperability; the OFA will not itself create industry standards

## Slide 23: Thank You