## Slide 1: OpenFabrics 2.0
Sean Hefty
Intel Corporation

## Slide 2: Claims
Verbs is a poor semantic match for industry standard APIs (MPI, PGAS, ...)
  Want to minimize software overhead
ULPs continue to desire additional functionality
  Difficult to integrate into existing infrastructure
OFA is seeing fragmentation
  Existing interfaces are constraining features
  Vendor specific interfaces

## Slide 3: Proposal
Evolve the verbs framework into a more generic open fabrics framework
  Fold in RDMA CM interfaces
  Merge kernel interfaces under one umbrella
Give users a fully stand-alone library
  Design to be redistributable
Design in extensibility
  Based on verbs extension work
  Allow for vendor-specific extensions
Export low-level fabric services
  Focus on abstracted hardware functionality

## Slide 4: Analysis A “Brief” Look at API Requirements
Datagram – streaming
Connected – unconnected
Client-server – point to point
Multicast
Tag matching
Active messages
Reliable datagram
Strided transfers
One-sided reads/writes
Send-receive transfers
Triggered transfers
Atomic operations
Collective operations
Synchronous - asynchronous transfers
QoS
Ordering – flow control
But, wait, there’s more!

## Slide 5: Observations
A single API cannot meet all requirements and still be usable
Any particular app is likely to need only a small subset of such a large API
Extensions will still be required
  There is no correct API!
We need more than an updated API – we need an updated infrastructure

## Slide 6: Proposed OpenFabrics Framework
Fabric Framework
OFA Provider
IB Verbs
Verbs Provider
Verbs
Fabric Interfaces
Transition from providing verbs API
to providing fabric interfaces

## Slide 7: Architecture
FI Framework
Vendor Provider
Fabric Interfaces
Dynamic Provider
OFA Provider
Usable as a stand-alone library
Can support external providers
Provides core functionality needed by providers
Exports control interface used to discover supported fabric interfaces
Defines fabric interfaces

## Slide 8: Fabric Interfaces
Fabric Interfaces (examples only)
Message Queue
Control
Interface
RMA
Atomics
Active Messaging
Tag Matching
Collective Operations
CM Services
Fabric Provider Implementation
Message Queue
CM Services
RDMA
Collective Operations
Control Interface
Framework defines multiple interfaces
Vendors provide optimized implementations

## Slide 9: Fabric Interfaces
Defines philosophy for interfaces and extensions
Exports a minimal API
  Control interface
Providers built into library
  Support external providers
Design to be redistributable
  Define guidelines for vendor distribution
  Allow for application optimized build
Includes initial objects and interface definitions

## Slide 10: Philosophy
Extensibility
  Easy to add functionality to existing or new APIs
  Ability to extend structures
Expose primitive network and fabric services
  Strike balance between exposing the bare metal, versus trying to be the high level API
  Enable provider innovation without exposing details to all applications
  Allow more innovation to occur without applications needing to change
Agile Interface

## Slide 11: Philosophy
Performance
  ≥ existing solutions
  Minimize control data to/from the library
  Allow for optimized usage models
  Asynchronous operation

## Slide 12: Thoughts
What possibilities are there if we move from 1.x to 2.0?
What if we don’t constrain ourselves?
  Remove full compatibility as a requirement
Work from a more ideal solution backwards
  See where we end up and take aim at compatibility from there

## Slide 13: Sending Using Verbs
struct ibv_sge {
uint64_t addr;
uint32_t length;
uint32_t lkey;
};
struct ibv_send_wr {
uint64_t wr_id;
struct ibv_send_wr *next;
struct ibv_sge *sg_list;
int num_sge;
enum ibv_wr_opcode opcode;
int send_flags;
uint32_t imm_data;
union {
struct {
uint64_t remote_addr;
uint32_t rkey;
} rdma;
struct {
uint64_t remote_addr;
uint64_t compare_add;
uint64_t swap;
uint32_t rkey;
} atomic;
struct {
struct ibv_ah *ah;
uint32_t remote_qpn;
uint32_t remote_qkey;
} ud;
} wr;
};
For a simple asynchronous send, apps need to provide this:
(I can’t read it either)
<buffer, length, context>
Verbs asks for this
Union supports other operations
More than a semantic mismatch
Notes: Expand example that this is swizled going directly to the hardware

## Slide 14: Sending Using Verbs
struct ibv_sge {
uint64_t addr;
uint32_t length;
uint32_t lkey;
};
struct ibv_send_wr {
uint64_t wr_id;
struct ibv_send_wr *next;
struct ibv_sge *sg_list;
int num_sge;
enum ibv_wr_opcode opcode;
int send_flags;
uint32_t imm_data;
...
};
Application request
<buffer, length, context>
Must link to separate SGL and initialize count
Requests may be linked - next must be set to NULL
3 x 8 = 24 bytes of data needed
SGE + WR = 88 bytes allocated
App must set and provider must switch on opcode
Must clear flags
28 additional bytes initialized
Significant SW overhead

## Slide 15: Alternative Model?
(*send)(fid, buf, len, flags, context);
(*sendto)(fid, buf, len, flags, dest_addr, addrlen, context);
(*sendmsg)(fid, *fi_msg, flags);
(*write)(fid, buf, count, context);
(*writev)(fid, iov, iovcnt, context);
What about an asynchronous socket-like OO-model?
Define extensible collection of interfaces suitable for sending and receiving messages
Optimized interfaces
Socket APIs have held up well against evolving networks

## Slide 16: Sending Using Verbs
union {
struct {
uint64_t remote_addr;
uint32_t rkey;
} rdma;
struct {
uint64_t remote_addr;
uint64_t compare_add;
uint64_t swap;
uint32_t rkey;
} atomic;
struct {
struct ibv_ah *ah;
uint32_t remote_qpn;
uint32_t remote_qkey;
} ud;
} wr;
Other operations handled similarly
Define RMA and atomic specific interfaces
Allow apps to ‘connect’ UD socket to specific destination

## Slide 17: Verbs Completions
struct ibv_wc {
uint64_t wr_id;
enum ibv_wc_status status;
enum ibv_wc_opcode opcode;
uint32_t vendor_err;
uint32_t byte_len;
uint32_t imm_data;
uint32_t qp_num;
uint32_t src_qp;
int wc_flags;
uint16_t pkey_index;
uint16_t slid;
uint8_t sl;
uint8_t dlid_path_bits;
};
Provider must fill out all fields, even if app ignores some
Developer must determine if fields apply to their QP
Single structure is 48 bytes – likely to cross cacheline boundary
App must check both return code and status to determine if a request completed successfully

## Slide 18: Verbs Completions
struct ibv_wc {
uint64_t wr_id;
enum ibv_wc_status status;
enum ibv_wc_opcode opcode;
uint32_t vendor_err;
uint32_t byte_len;
uint32_t imm_data;
uint32_t qp_num;
uint32_t src_qp;
int wc_flags;
uint16_t pkey_index;
uint16_t slid;
uint8_t sl;
uint8_t dlid_path_bits;
};
Let application identify needed data
Report unexpected errors ‘out of band’
Separate addressing data from completion data
Use compact structures with only needed data exchanged across interface

## Slide 19: Proposal Summary
Merge existing APIs into a cohesive interface
Abstract above the hardware
  Enable optimizations to reduce memory writes, decrease allocated buffer space, minimize cache footprint, and avoid code branches
Focus APIs on the semantics and services offered by the hardware and not the implementation
  Message queues and RDMA, versus QPs
  Minimize API churn for every hardware feature

## Slide 20: Moving Forward
Critical to have wide support and shared ownership
  General agreement on approach
Define control interfaces and object models
  Effectively instantiate the framework
Describe fabric interfaces
Success ultimately depends on adoption – vendors AND users
Use open source processes

## Slide 21: Open Fabrics 2.0
libfabric - Proposal

## Slide 22: Path Forward
Framework must efficiently support existing HW
  Compelling adoption and migration story
  Some legacy elements
Move focus from HW to application semantics
  Make the users happy
Provide clear path for moving applications and providers forward

## Slide 23: Path Forward
Reach agreement on framework infrastructure
  Control interfaces and basic objects
Define a couple of simple API sets
  Derived from current usage models
  E.g. CM and message queue APIs
Design application tuned APIs
Proposed time-driven release schedule
  Target initial release within 12 months

## Slide 24: Philosophy
Administrator configured
  Based on Linux networking options
  Simplify application use
  Provider defined defaults with administrator control

## Slide 25: Architecture
libfabric
Vendor Provider
Fabric Interfaces
Dynamic Provider
OFA Provider

## Slide 26: Control Interface
fi_getinfo
Discover fabric providers and services
Identify resources and addressing
fi_endpoint
Allocate fabric communication portal
fi_open
Open resource domain and interfaces
fi_register
Dynamic providers publish control interfaces
FI Framework
fi_getinfo fi_freeinfo
fi_endpoint fi_open
fi_register

## Slide 27: Object Model
Resource Domain
Protection Domain
Shared Receive Queues
Event Collectors
Address Vectors
Fabric Endpoint
Unbound Interfaces
Kernel uAPI
Provider I/F
Fabric Interfaces
Boundary of resource sharing
Binds to resources
Identified by name
Helper interfaces and provider specific capabilities

## Slide 28: Fabric Interface Descriptors
FID
Endpoint
Datagram
Message queue
Event collector
CQ
CM
Address vector
Maps
Tables
Interface
uverbs
ucma
Domain
Shared resources
Counter
Memory Descriptors
Based on object-oriented programming
Derived objects define interfaces
  New interfaces exposed
  Define behavior of inherited interfaces
  Optimize implementation
FID
  Base object identifier
  Control interfaces

## Slide 29: Fabric Endpoint Interfaces
Type
Protocol
Address
Base EP API
CM
Message Transfers
RMA
Tagged
Atomics
Collectives
Properties
Interfaces
Endpoint
Evolution of RDMA CM & QP
Interfaces enabled based on protocol
Interface implementation optimized based on endpoint properties

## Slide 30: Event Collectors
Format
Wait Object
Domain
Context only
Data
Tagged
Addressing
CM
Error
None
fd
mwait
Properties
Interface Details
EC
Common abstraction for asynchronous events
User specified wait object
Optimized event data
Optimize interface around reporting successful operations

## Slide 31: Address Vectors
Format
INET
INET6
IB
FI Address
AV index
Properties
Interface Details
AV
Maps network addresses to fabric specific addressing
Encapsulates fabric specific requirements
- Address resolution
- Route resolution
- Address handles
Can be referenced for group communication
Configure resource domain to use specific address formats

## Slide 32: Compatibility
Support migration path for apps
  Allow software to evolve to new framework selectively
  Goal: increase adoption rate
Define ‘compatibility’ mode
  Applications must recompile
  No source changes
  Can selectively adopt new interfaces
  Goal: fully compatible

## Slide 33: Moving Forward
Involve key users and contributors
Consider alternates
  Identify commonalities and differences
  Resolve issues
Discuss and refine details
  Moving in the desired direction
Collect, analyze, and discuss proposals

## Slide 34: Fabric Information
struct fi_info {
struct fi_info *next;
size_t size;
uint64_t flags;
uint64_t type;
uint64_t protocol;
uint64_t interfaces;
enum fi_iov_format iov_format;
enum fi_addr_format addr_format;
enum fi_addr_format info_addr_format;
size_t src_addrlen;
size_t dst_addrlen;
void *src_addr;
void *dst_addr;
size_t auth_keylen;
void *auth_key;
int shared_fd;
char *domain_name;
size_t datalen;
void *data;
};

## Slide 35: Base Fabric Descriptor
struct fi_ops {
size_t size;
int (*close)(fid_t fid);
int (*bind)(fid_t fid, struct fi_resource *fids, int nfids);
int (*sync)(fid_t fid, uint64_t flags, void *context);
int (*control)(fid_t fid, int command, void *arg);
};
struct fid {
int fclass;
int size;
void *context;
struct fi_ops *ops;
};

## Slide 36: FI - Communication
enum fid_type {
FID_UNSPEC,
FID_MSG,
FID_STREAM,
FID_DGRAM,
FID_RAW,
FID_RDM,
FID_PACKET,
FID_MAX
};
enum fi_proto {
FI_PROTO_UNSPEC,
FI_PROTO_IB_RC,
FI_PROTO_IWARP,
FI_PROTO_IB_UC,
FI_PROTO_IB_UD,
FI_PROTO_IB_XRC,
FI_PROTO_RAW,
FI_PROTO_MAX
};
#define FI_PROTO_MSG (1ULL << 8)
#define FI_PROTO_RMA (1ULL << 9)
#define FI_PROTO_TAGGED (1ULL << 10)
#define FI_PROTO_ATOMICS (1ULL << 11)
/* Multicast uses MSG ops */
#define FI_PROTO_MULTICAST (1ULL << 12)
/*#define FI_PROTO_COLLECTIVES (1ULL << 13)*/

## Slide 37: FI – Communication - MSG
struct fi_ops_msg {
size_t size;
ssize_t (*recv)(fid_t fid, void *buf, size_t len, void *context);
ssize_t (*recvmem)(fid_t fid, void *buf, size_t len, uint64_t mem_desc,
void *context);
ssize_t (*recvv)(fid_t fid, const void *iov, size_t count,
void *context);
ssize_t (*recvfrom)(fid_t fid, void *buf, size_t len,
const void *src_addr, void *context);
ssize_t (*recvmemfrom)(fid_t fid, void *buf, size_t len,
uint64_t mem_desc,
const void *src_addr, void *context);
ssize_t (*recvmsg)(fid_t fid, const struct fi_msg *msg,
uint64_t flags);
/* corresponding send calls */
};

## Slide 38: FI – Communication
struct fid_socket {
struct fid fid;
struct fi_ops_sock *ops;
struct fi_ops_msg *msg;
struct fi_ops_cm *cm;
struct fi_ops_rma *rma;
struct fi_ops_tagged *tagged;
/* struct fi_ops_atomics *atomic; */
};