## Slide 1: New Direction Proposal: An OpenFabrics Fabric Manager Framework Proposal
August 13, 2020
www.openfabrics.org

## Slide 2: OFA Board Ask
Create an OpenFabrics Management Working Group to:
  Develop, test, and distribute:
    An extensible, open source framework that provides access to high-performance fabric management interfaces and services.
    Extensible, open source interfaces aligned with orchestration and workload management application needs for high-performance fabric management services.
www.openfabrics.org
Notes: Expect these numbered bullets are going to be core to the charter for the Work Group which we are proposing be created.

## Slide 3: Problem Statement
HPC clusters and cloud computing environments are running increasingly diverse and dynamic workloads
More numbers of and types of messaging and storage fabrics
New interconnect capabilities such as memory semantic fabrics
Orchestration tools and workload managers do not deal well with multiple fabrics
There is an explosion of fabrics, resources, and clients, yet no common fabric manager interfaces and fabric models available
www.openfabrics.org
Notes: This slide is focusing on the need of orchestration and workload manager tools for a common fabric services abstraction
<try to get past this slide and on to the visual version as expediently as possible>

## Slide 4: The Fabric Admin Problem
Fabric Services
The Fabric Admin Problem
  Orchestration tools, workload managers, and middleware request configuration changes
  These tools need an abstracted view of fabric services
  Each fabric has different attributes
  Each fabric model is different
  Each fabric manager API set is different
  Only Ethernet is reasonably well understood by tools and apps
  Pre-configured clusters, pods, partitions, vLANs, or subnets required to avoid manual configuration at job launch
  No common model of generic fabric services
  No common interfaces to manipulate fabric resources
Need a common interface
Slurm
User APPs & Libraries
Gen-Z
Fabric Manager
Gen-Z
HW
Fabric Services
IB
Ethernet
…
Gen-Z
Ethernet
Fabric Managers
Eth
HW
IB
Fabric Manager
…
Fabric Manager
IB
HW
…
HW
Fabric Services
Fabric Services
AWS
PBS
Kubernetes
Orchestration Managers
Proprietary
Fabric Manager
AWS
HW
Notes: Most tool stacks, orchestration layers, app libraries, etc. share a need to request specific resources and configurations from a fabric through some sort of fabric services interface.
Many different apps, libraries, automation tools
Many different fabrics
Many different fabric management stacks and associated CLIs or GUIs with many APIs
However, each fabric implements these management functions differently.
The orchestration and composing tool ‘applications’ need a common interface to invoke common fabric management functions.
Fortunately, the OFA knows a thing or two about such things.
… next slide

## Slide 5: So what do we do?
Hardware Layer
Application Interface
Application and
Mgmt Application
layer
Provider Layer
Examine the classes of management applications that are important to users of fabrics.
Let the applications drive the appropriate interface definitions.
This, in turn, drives the necessary management features that the fabric plug in should support.
Fabric Provider maps high level requests to fabric specific operations
www.openfabrics.org
Notes: We need to determine a fundamental, yet extensible set of fabric management services interfaces that are common, and available to the tools and apps in the layers above.
Then we use these interface definitions to drive the mgmt features which the fabric specific plug-ins should support.

## Slide 6: Fabric Interfaces Examples
Standardized Fabric Manager Framework Interfaces (examples only)
Peer Address Lookup
Fabric & Provider info
Partition Mgmt
Inventory
Authent-ication
Link State Mgmt
Events & Logs Registration
Security
Fabric Provider Implem-entation
Framework defines multiple standardized interfaces
Fabric Provider Implem-entation
Fabric Provider Implem-entation
Fabric Provider Implem-entation
Fabric Provider Implem-entation
Fabric Provider Implem-entation
Vendors provide optimized implementations
Notes: The golden orange boxes describe several common fabric services that upper layer tools often want to access. EX: inventory, peer lookup, partitioning of resources
The fabric manager framework would offer common interfaces (northbound, or from the top of the green box)
The framework would translate the requests into more specific requests appropriate for providers to digest
Fabric specific providers create fabric specific traffic to configure their fabrics as needed
Next slide is a more detailed example walk through that better defines the framework/provider nature of the OpenFabrics Fabric Manager Framework

## Slide 7: Fabric Administration Workspace
Administration Domain
abstract
manipulations
SLURM
PBS
Kubernetes
Provider
Framework
OFFM Domain
Hardware
Partition Mgmt
Events & Logs
Authentication
Peer Address Lookup
Gen-Z
Slingshot
IB
Create Zone
Create Partition
Redfish
Model
Native
Model
Create Partition
Create zone
Create zone
Create zone
Notes: Left side is the user/admin/orchestration/automation domain(s)
Right side is the hardware that makes up the fabric and the resources that are accessed thereon
The middle is a representation of the functional blocks making up the OpenFabrics Fabric Management Framework
On the left, various workload managers are represented.
Any entity (SW tool, admin GUI, shell script via CLI) may need to create a virtual platform, pod, cluster, partition, vLan, job queue, subnet or other name for a set of resources that are connected together to enable some workload(s) to execute while being isolated from other jobs.
Such an entity needs a common taxonomy for describing the resources needed in the set and how the connections among them are to behave.
We are proposing to use the DMTF’s Redfish standards to model the fabric and its resources, and to provide the RESTful interfaces through which the entities on the left can learn of the modelled resources and create such a set of fabric resources.
Redfish currently has an object called a ‘zone’ that contains a list of the fabric endpoints which may be connected to each other. Zones can be used to enumerate the members of a vLAN, or the resources of a virtual platform.
Entities on the left hand side make a common call to create a Redfish ‘zone’.
The framework will update the Redfish model for the given fabric(s) and exchange the appropriate details with the fabric specific provider(s)
The Providers are responsible for updating any native models they maintain of their fabric and to issue the appropriate traffic to the fabric hardware

## Slide 8: Proposal
Develop the OFM interfaces based on management tool needs
Create work register between OFA and DMTF
  Evolve the Redfish fabrics model and schema to accommodate the defined framework interfaces
  Evolve the Redfish model and schema to ease translation of existing fabric models for providers
Design in flow-through Provider optimizations
Design in support for memory semantic features
Design in extension support
Export low-level fabric services
  Focus on abstracted fabric hardware functionality

## Slide 9: Next Steps
Get moving on developing this Framework!
Recommend starting a WG to focus development efforts
Develop a work register with DMTF
Create an OpenFabrics Management Framework Working Group to:
  Develop, test, and distribute:
    An extensible, open source framework that provides access to high-performance fabric management interfaces and services.
    Extensible, open source interfaces aligned with orchestration and workload management application needs for high-performance fabric management services.
www.openfabrics.org

## Slide 10: Thank You
www.openfabrics.org

## Slide 11: Participants
Forest Godfrey HPE
Barry McAuliffe HPE
David Collins Sandia
Doug Ledford Red Hat
Gilad Shainer Mellanox
Hassan Reza University of
North Dakota
Jim Foraker Lawrence Livermore
Jeff Hilland HPE/DMTF
Jim Ryan
John Mayfield HPE/DMTF
Kurt Bowman Dell
Mike Aguilar Sandia
Paul Grun
Russ Herrell HPE
Sean Hefty Intel
www.openfabrics.org
www.openfabrics.org
Notes: Just a list of participants and the companies they represent.
Company reps also serve on Gen-Z and DMTF work groups and contribute expertise in those areas