## Slide 1
Stan Smith Intel SSG/DPD
March, 2015
Kernel OpenFabrics Interface
Server End point setup

## Slide 2: Steps
The Big Picture
  Initialization
  Server connection setup
  Client connection setup
  Connection finalization
  Data transfer
  Shutdown
Current State
  Completed: fi_getinfo(), fi_fabric(), fi_domain()
Server connection setup:
  fi_passive_ep() *pep – create a passive endpoint.
  fi_eq_open() *event queue – where connection requests appear.
  fi_pep_bind() bind EQ to passive end-point.
  fi_listen(pep) post a listen for the passive endpoint.
  fi_eq_sread(eq) blocking wait for connection request(s).

## Slide 3: fi_passive_ep()
Create a passive endpoint. Passive endpoints belong to a fabric domain and are used to listen for incoming connection requests.
struct fid_pep *pep;
int fi_passive_ep( struct fid_fabric *fabric, struct fi_info *info,
struct fid_pep **pep, void *context );
Arguments:
*fabric – fabric instance.
*info – application selected fi_info record.
**pep (out) passive endpoint pointer.
*context – domain event context.
Return:
  rc == 0 defines success.

## Slide 4: fi_eq_open()
Create an event queue used in waiting for and accepting connection requests.
int fi_eq_open(struct fid_fabric *fabric, struct fi_eq_attr *attr,
struct fid_eq **eq, void *context)
Arguments:
*fabric – opened fabric instance
*attr – EQ attributes
**eq – output event queue ptr.
*context – application supplied value, returned in EQ events.
Return:
0 == success.

## Slide 5: struct fi_eq_attr
struct fi_eq_attr {
size_t size; # min EQ depth
uint64_t flags; # operational flags: FI_WRITE, can write to EQ
enum fi_wait_obj wait_obj; # wait object type:
FI_WAIT_NONE async
FI_WAIT_UNSPEC(blocking)
FI_WAIT_SET, use existing wait_set.
int signaling_vector; # core where CQ interrupts are directed.
struct fid_wait *wait_set; # existing wait_set pointer;
# requires FI_WAIT_SET
}

## Slide 6: fi_pep_bind()
Associate a passive endpoint with an event queue
int fi_pep_bind(struct fid_pep *pep, struct fid *fid, uint64_t flags)
Arguments:
*pep – existing passive endpoint
*fid – EQ->fid to bind to the passive endpoint.
flags – operational flags.
Return
  0 == success

## Slide 7: fi_eq_sread()
Blocking read of one event from event queue.
int fi_eq_sread(struct fid_eq *eq, uint32_t *event, void *buffer, size_t len,
int timeout, uint64_t flags)
Arguments:
*eq – opened Event Queue
*event – reported event ID.
*buffer – event format defined via fi_info->ep_attr.protocol
len – sizeof( eq event ).
timeout – default units (milliseconds) or flags defines units.
flags – operational flags:
    FI_PEEK – read without consuming the event.
    FI_TIME_US – micro-seconds
    FI_TIME_MS – milli-seconds
Return: number of bytes written to buffer; at most 1 event.

## Slide 8: Infiniband Server RC example
struct fi_fid_pep *pep;
struct fi_eq_attr eq_attr = {10, 0, FI_WAIT_UNSPEC, 0, NULL };
struct fi_fid_eq *eq;
uint32_t event_id;
struct fi_eq_cm_entry event; // format derived from fi_info. ep_attr->protocol =
// FI_PROTO_RDMA_CM_IB_RC;
ret = fi_passive_ep(fabric, provider, &pep, 0xCafeBabe );
ret = fi_eq_open(fabric, &attr, &eq, 0);
ret = fi_pep_bind( pep->fid, eq->fid, 0);
ret = fi_listen(pep)
ret = fi_eq_sread(eq, &event_id, (void*)&event, sizeof(event), 20000, FI_TIME_MS);
// blocked waiting for a client connection.

## Slide 9
Thank you.