## Slide 1: RDMA with byte-addressable PM RDMA Write Semantics to Remote Persistent Memory An Intel Perspective when utilizing Intel HW
12/02/14
Chet Douglas, DCG Crystal Ridge PE SW Architecture

## Slide 2: RDMA with DRAM – Intel HW Architecture
CPU
ADR Domain
ADR – Asynchronous DRAM Refresh
  Allows DRAM contents to be saved to NVDIMM on power loss
  ADR Domain – All data inside of the domain is protected by ADR and will make it to NVM before supercap power dies. The integrated memory controller is currently inside of the ADR Domain.
IIO – Integrated IO Controller
  Controls IO flow between PCIe devices and Main Memory
  Contains internal buffers that are backed by LLC cache. “Allocating write transactions” from the PCI Root Port will utilize internal buffers backed by LLC core cache.
  Data in internal buffers naturally aged out of cache in to main memory
  Enable/Disable via BIOS setting per Root PCI Port
DDIO – Data Direct IO
  Allows Bus Mastering PCI & RDMA IO to move data directly in/out of LLC Core Caches
  Enable/Disable at platform level via BIOS setting
IIO
PCI Root Port
MAIN Memory
PCI Func
PCI Func
PCI Func
PCI Func
RNIC
Internal BUFFERS
Allocating Write Transactions
LLC
CORE
CORE
CORE
CORE
DDIO
PCI BM DMA Flow
RNIC RDMA Flow
DDIO ON Flow
DDIO OFF Flow
iMC

## Slide 3: RDMA with byte-addressable PM – Intel HW Architecture
CPU
Short Term NVM Considerations
  With ADR, No DDIO
    Disable DDIO
      Requires BIOS Enabling
    Enable “non-allocating Write” transactions for Root PCI Port to IIO
      Requires BIOS Enabling
      Forces RDMA Write data directly to iMC
      Enable on PCI Root Port with RNIC
    Follow RDMA Write(s) with RDMA Read to force remaining IIO buffer write data to ADR Domain
      Since RDMA Write and Read are silent, there is little or no change to the SW on the node supplying the Sink buffers for RDMA Write
IIO
PCI Root Port
RNIC
Internal BUFFERS
Non-Allocating Write Transactions
LLC
CORE
CORE
CORE
CORE
DDIO
RNIC RDMA Read Flow
RNIC RDMA Write Flow
Write Data forced to persistence by ADR Flow
iMC
NVM
ADR Domain
RDMA Write Data forced to ADR Domain by RDMA Read Flow

## Slide 4: RDMA with byte-addressable PM – Intel HW Architecture
CPU
Short Term NVM Considerations
  Without ADR, No DDIO
    Disable DDIO
      Requires BIOS Enabling
    Enable “non-allocating Write” transactions for Root PCI Port to IIO
      Requires BIOS Enabling
      Forces RDMA Write data directly to iMC
      Enable on PCI Root Port with RNIC
    Follow RDMA Write(s) with RDMA Read to force remaining IIO buffer write data to ADR Domain
    Follow RDMA Read with Send/Receive to get callback to force write data in the iMC to become persistent
      ISA - PCOMMIT/SFENCE – Flush iMC and make data persistent
IIO
PCI Root Port
RNIC
Internal BUFFERS
Non-Allocating Write Transactions
LLC
CORE
CORE
CORE
CORE
DDIO
RNIC RDMA Send/Receive Flow
RNIC RDMA Write Flow
Send/Receive Callback PCOMMIT/SFENCE Flow
iMC
NVM
ADR Domain
RDMA Write Data forced to iMC by Send/Receive Flow

## Slide 5: RDMA with byte-addressable PM – Intel HW Architecture
CPU
Short Term NVM Considerations
  Without ADR, With DDIO
    Use standard “allocating Write” transactions for Root PCI Port to IIO
    Follow RDMA Write(s) with Send/Receive to get local callback to force write data from CPU Cache in to the iMC and to make write data in the iMC persistent
      Send/Receive will contain list of cache lines that were written
      ISA – CLFLUSHOPT/SFENCE – Flush CPU cache lines and wait for flush to complete (invalidates cache contents). The list of cache lines from the Send message is used to identify the cache lines that need to be flushed.
      ISA - PCOMMIT/SFENCE – Flush iMC and make data persistent
      Internal IIO buffers will be flushed as part of CLFLUSHOPT allowing “allocating writes” to be used.
IIO
PCI Root Port
RNIC
Internal BUFFERS
Allocating Write Transactions
LLC
CORE
CORE
CORE
CORE
DDIO
RNIC RDMA Send/Receive Flow
RNIC RDMA Write Flow
Send/Receive Callback CLFLUSHOPT/SFENCE Flow
iMC
NVM
ADR Domain
RDMA Write Data forced to iMC by Send/Receive Flow
Send/Receive Callback PCOMMIT/SFENCE Flow

## Slide 6: RDMA with byte-addressable PM – Intel HW Architecture
Long Term NVM Considerations
  Just ideas at this point….
    ADR HW:
      Increase ADR Domain to include LLC and IIO Internal Buffers
    IIO HW:
      Make HW aware of persistent memory ranges
      If PCI Read is required, automate read at end of RDMA Write(s), how to indicate end of write(s), hold off last write completion until read complete
      With ADR:
        Force write data to iMC before completing write transaction
        Utilize new transaction type to flush list of persistent memory regions to iMC before completing new transaction
      Without ADR:
        Force write data to iMC and then to persistence before completing write transaction
        Utilize new transaction type to flush list of persistent memory regions to iMC and then to persistence before completing new transaction
    DDIO HW:
      Make HW aware of persistent memory ranges and enable DDIO for DRAM and disable for persistent memory transactions on the fly