## Slide 1: IB ACM InfiniBand Communication Management Assistant (for Scaling)
Sean Hefty

## Slide 2: Problem
MPI job startup places a huge burden on the fabric
Need to resolve addresses
Need to resolve paths

## Slide 3: Problem Address Resolution
ARP for address resolution
  ARP storm as all nodes try to discover other nodes
    Number of outstanding ARP requests = O(n2)
    May require pre-loading ARP cache before starting MPI job
  ARP replies require path record queries!
  ARP entries timeout across the subnet
    1000 nodes  1 million ARP entries subnet wide
    15 minute timeout  1000 entries timeout per second
    24 hour timeout  12 entries timeout per second
    Even with a 24 hour ARP entry timeout, 7200 entries will timeout during a 10 minute MPI run!
No easy solution, but workable in practice

## Slide 4: Problem Path Resolution
Centralized SA hinders scalability
Number of outstanding queries = O(n2)
Queries take minutes to complete
  If apps actually wait that long
  (Think of how many ARP entries just timed out!)
  Responses are not shared
Standard path record query mechanisms simply do not work at scale

## Slide 5: Solution IB ACM
Addresses connection setup scalability issues
Service / daemon providing:
Address resolution
  ARP like protocol over IB multicast
  Names may be host names, IP addresses
Route resolution
  Construct or query for path records
  Path record caching

## Slide 6: Solution ACM for Address Resolution
Wait, why duplicate ARP mechanisms?
IPoIB issues path record queries as part of its ARP implementation
Store address and route data together
  Timeout data together
  Under certain conditions, we can resolve address and route data without using SA queries
We can obtain additional information about the remote device
  E.g. maximum RDMA capabilities
Restrict the number of outstanding address resolution requests on the subnet to O(n)

## Slide 7: Solution ACM for Route Resolution
Is ACM a path record cache?
Yes, but also an open source framework for addressing scalability issues
  May be able to construct path records without querying the SA
Integrates with the librdmacm to make its use transparent to the user
Restricts the number of outstanding SA queries from the subnet to O(n)

## Slide 8: Usage Model
Recommended use is via librdmacm
  Requires ‘--with-ib_acm’ compile option
    Temporary requirement, will be removed once ACM is more proven
  Falls back to normal resolution on failures
    Unable to contact local or remote ib_acm service
    Failure to resolve address or path information
    Small latency hit if librdmacm compiled with ACM support, but service is not running

## Slide 9: Usage Model
rdma_resolve_route
  All existing librdmacm apps can take advantage of path record caching
  Path data is obtained from ib_acm service and kernel is configured to use it
    ib_acm lookup is synchronous
  Requires kernel 2.6.33 (OFED 1.5.2) or newer
rdma_resolve_addr still ends up going through ARP :P

## Slide 10: Usage Model
rdma_getaddrinfo
  Supports address and route resolution
    Kernel support to make use of address resolution is pending (AF_IB patch set)
  Can act as a simple (i.e. dumb) path record query interface
    For apps that manually configure their QPs, but require path records (specifically SL data) from the SA to avoid subnet deadlock
  NODELAY flag
    Quick check against cached data
    Kicks off ACM resolution protocols in background
    Future lookups can find cached data

## Slide 11: Usage Model
ib_acm may be accessed directly via a socket interface
  Not recommended
  Protocol is defined by acm.h header file, but is not documented
  librdmacm and ib_acme may be used as guides

## Slide 12: ACM Service
Listens on TCP socket
Simple request / reply protocol
Input:
  Name, IP address, partial path record
  Destination and optional source
Output:
  Set of path records
    Forward, reverse, alternates, CM paths
  Current implementation is 1
    Path must be fully reversible

## Slide 13: ACM Service Examples
src = [192.168.0.2]
dst = 192.168.0.3
Path record with
SGID / DGID
Path Record
Path Record
IB ACM
librdmacm
(rdma_getaddrinfo)

## Slide 14: ACM Operation
All ACM services join multicast groups
  Groups differ by pkey, rate, MTU, type of service
  All services must join 1 common group
  All traffic occurs on common group
ACM receives client request
Initiator broadcasts destination address on common multicast group
All peer ACM services cache source data

## Slide 15: ACM Operation
Target service queries SA or constructs path record to initiator
  See next slide
Target service responds with IB address
Initiator caches response address
Initiator queries SA or constructs path record to target
ACM responds to client request

## Slide 16: ACM Operation
Query SA for path data
  Required for certain fabric topologies to avoid deadlock
Construct path record based on common multicast group supported by source and destination
  Can be more efficient
  Once multicast groups are configured, avoids querying the SA

## Slide 17: ACM Communication
Defines application specific MADs
  Uses management class 44
Allocates a UD QP
Protocol is defined internal to ACM service
  Defined in internal header files
  Undocumented

## Slide 18: ACME
Multi-purpose ACM test and configuration application
Verifies path data from ACM against SA path records
  Can be used to validate if multicast resolution protocol is usable
May be used to pre-load cache
Generate configuration files

## Slide 19: ACM Configuration
Users may override default ACM configuration options through the use of configuration files
Default files can be generated using the ib_acme utility
  acm_addr.cfg
    Contains local address data
    File will be unique per node
  acm_opts.cfg
    Contains ACM service options
    Likely the same across an entire cluster

## Slide 20: ACM Configuration
Address assignments
  <device, port, pkey, name>
  Name is usually host name or IP address
  Pkey can be use for QoS
Logging location and details
Timeout / retry settings
Outstanding requests limits
  To SA or peer ACM services
  Restricts the number of outstanding requests on the subnet

## Slide 21: Work In Progress
Validate concepts, performance, and scalability
  Initial testing is positive
Support for dynamic changes is limited
  Handles port up/down events
  Does not respond to local IP address or hostname changes
Want to obtain path data progressively
  Pre-load cache using ib_acme
  Save / restore data between reboots

## Slide 22: Work In Progress
Cached data not invalidated
  Must stop / restart service
  Proposal is to invalidate data based on CM timeouts
    Dependent on kernel changes
QoS support controlled by SA
  Addresses / names map to specific pkey values
  A QoS scheme based on pkeys would work best

## Slide 23: Pending Work AF_IB Support
Allows direct IB addressing with transport independent rdma_getaddrinfo interface
Desired for librdmacm to make use of ACM address resolution
Removes librdmacm requirement for ipoib
Provides greater flexibility moving forward to support alternate paths

## Slide 24: Pending Work MAD Snooping
Invalidate cache based on local events
  CM timeouts, rejects
Avoid registering for SA events
  Data is invalidated based on local events only
Capture path data from other applications
  ipoib, srp, iser, rds, etc.